## Slide 1: Permit to Work Process​ HSE GROUP RULE (CR-GR-HSE-402)
EXECUTIVE SUMMARY
This rule defines the minimum HSE requirements to be respected when preparing, approving, coordinating and executing work.

## Slide 2
Purpose : This rule defines the minimum HSE requirements to be respected when preparing, approving, coordinating and executing work, and in particular the organisation and monitoring of the permit to work process, as well as the competencies of the personnel involved.
Scope of Application: Applicable to all operated Group entities and affiliates.
Replaces:
  CR RC EXP 034 Permit to Work Process
  CR EP HSE 036 Permit to Work
  CR G&P HSE 031 Permit to Work
  CR MS HSEQ 202 High-risk operations and works (Section 5. Work Autorisation/Work Permits)
REFLEX publication date : 30/09/2019
Effective date : 6 months following date of publication.

## Slide 3
Overview of the permit to work process
Organisation of the permit to work process
Preparation
Coordination
Execution
End of work and permit closure
Approval and acceptance
Audits and performance improvement
Figure 1: Main steps in the permit to work process

## Slide 4
REQUIREMENT OVERVIEW : Organisation of the permit to work process
Permit to Work Procedure (Requirement 3.1.1)
The permit to work process is described in a documented procedure to include the requirements of this rule as a minimum.
GRP and MS : New requirement
Roles and Assignments (Requirement 3.1.2)
The distribution of roles and assignments for personnel involved in the permit to work process, as well as the possibilities for delegation, is clearly defined and communicated to the personnel concerned in the entity or affiliate, as well as to contractors so that they can inform their personnel.
EP-RC-MS : Roles are defined but not the delegations GRP : New requirement
Separation of Roles (Requirement 3.1.3)
A person cannot approve or issue a permit to work for work that he is to perform.
GRP : New requirement

## Slide 5
REQUIREMENT OVERVIEW : Organisation of the permit to work process
Delimitation of a Zone Under the Control of the Issuing Authority (Requirement 3.1.4)
The accurate delimitation of zones and their interconnections is defined and communicated to the personnel concerned in the entity or affiliate, as well as to contractors so that they can inform their personnel.
Each zone reports to a single permit to work issuing authority for a given period.
New requirement for all branches RC : Requirement important for determining the responsibilities of interconnecting units/off sites/utilities (flare network/units)
Training and Authorisation (Requirement 3.1.5)
Everyone with a role in the permit to work process is trained and authorised to conduct their role. The authorisation is documented.
A list of trained and authorised personnel is kept up to date.
The frequency of refresher training, at least every 5 years, is determined by the permit to work procedure.
EP-RC-MS : contractor training requirement is new GRP : New requirement

## Slide 6
REQUIREMENT OVERVIEW : Organisation of the permit to work process
Permit to Work Validity Period (Requirement 3.1.6)
The maximum validity period for a permit to work is defined by the permit to work procedure.
When the validity period of a permit to work has expired, the work concerned cannot begin or be continued without a new permit to work.
GRP : New requirement
Permit to Work and Certificate Types (Requirement 3.1.7)
The permit to work procedure defines the different types of applicable permits to work and the work that requires certificates.
If required, the permit to work is accompanied by all the necessary certificates.
RC-MS : establish a list of works that requires certificates GRP : New requirement

## Slide 7
REQUIREMENT OVERVIEW : Organisation of the permit to work process
Simplified Permit to Work (Requirement 3.1.8)
A “simplified” permit to work is used only for recurrent and low-risk work that does not generate any co-activity or simultaneous operations.
The permit to work procedure includes an exhaustive list of work covered by a simplified permit to work. The list is established after a specific risk analysis and approved by the appropriate line manager at least once a year.
GRP-MS-RC : New requirement
Work Authorised Without a Permit to Work (Requirement 3.1.9)
The rules for preparing and approving work that can be executed without a permit to work is defined in the permit to work procedure.
The exhaustive list of work that can be executed without a permit to work is drawn up according to the risk analysis. It is reviewed and approved by the appropriate line manager at least once a year.
RC-MS : establish a list of works that can be executed without a permit to work GRP : New requirement

## Slide 8
REQUIREMENT OVERVIEW : Permit to Work Preparation
Risk Analysis for the Permit to Work (Requirement 3.2.1)
A permit to work is based on a risk analysis.
GRP : New requirement
Joint Visit for “High Risk Work” (Requirement 3.2.2)
For “high risk work” the approving authority and the performing authority visit the work site as part of the permit to work preparation process.
EP-RC-MS : the definition of high risk work list is a new requirement GRP : New requirement
Organisation of the permit to work process
Preparation
Coordination
Execution
End of work and permit closure
Approval and acceptance
Audits and performance improvement

## Slide 9
REQUIREMENT OVERVIEW : Permit to Work Preparation
Permit to Work Content (Requirement 3.2.3)
Before approval, a permit to work includes at least the following information:
Identification of the performing authority;
Description of the work to be performed;
Work site;
Identification of the equipment concerned, if applicable;
Work execution dates;
Validity period of the permit;
Tools and means used;
Risks identified in the risk analysis and the risk control measures to be applied;
References for supporting documentation if applicable.
GRP : New requirement

## Slide 10
REQUIREMENT OVERVIEW : Approval and Acceptance of the Permit to Work
Permit to Work Approval and Acceptance (Requirement 3.3.1)
The permit to work is approved by the approving authority and accepted by the performing authority.
Any change to the terms of the permit requires re-approval from the approving authority and re-acceptance from the performing authority.
GRP : New requirement
Organisation of the permit to work process
Preparation
Coordination
Execution
End of work and permit closure
Approval and acceptance
Audits and performance improvement

## Slide 11
REQUIREMENT OVERVIEW : Coordination
Permit to Work Coordination (Requirement 3.4.1)
The number of permits to work to be issued for a zone as well as the risks related to simultaneous operations or co-activities are taken into account when coordinating the planned work.
A list of approved permits to work is then established and is communicated to the issuing authority.
EP-RC-MS : taking into account the number of permits to be issued is a new requirement GRP : New requirement
Organisation of the permit to work process
Preparation
Coordination
Execution
End of work and permit closure
Approval and acceptance
Audits and performance improvement

## Slide 12
REQUIREMENT OVERVIEW : Execution
Issuing Permits to Work (Requirement 3.5.1)
At least once a day, any start of work execution is subject to a prior issue of the permit to work by the issuing authority and its countersignature by the performing authority.
For “high risk work”, the permit is issued once the execution conditions and risk control measures have been checked on the work site by the issuing authority or the checker.
RC-MS : issuing the Permit once the execution conditions and risk control measures have been checked on the work site for “high risk work” is a new requirement GRP : New requirement
Organisation of the permit to work process
Preparation
Coordination
Execution
End of work and permit closure
Approval and acceptance
Audits and performance improvement

## Slide 13
REQUIREMENT OVERVIEW : Execution
Safety Green Light / Safety Talk Before Starting Work (Requirement 3.5.2)
Before start-up or restart of the work, or before any shift change, the performing authority explains to all workers, at the location of the work site, the operating procedure, the work environment, the risks identified in the permit to work and the associated risk control measures.
This safety talk is documented and signed by the performing authority and by each worker.
GRP-MS-RC : New requirement
Availability of the Permit to Work on the Work Site (Requirement 3.5.3)
During the execution of the work, the permit to work and associated certificates are permanently accessible to all crew members on the work site.
GRP-MS-RC : New requirement

## Slide 14
REQUIREMENT OVERVIEW : Execution
Work Site Monitoring (Requirement 3.5.4)
During the execution of the work, monitoring of the work site is set up by the performing authority.
In addition, work site monitoring is also performed by the issuing authority each time it is required by the permit to work.
New requirement for all branches
Suspension of the Permit to Work (Requirement 3.5.5)
The work and its associated permit are suspended in the following cases:
General alarm;
Specific instruction to stop works, including by a Stop Card;
Failure to comply with one of the requirements imposed in the permit to work;
Modification of the work execution procedure;
Change in the work site environment;
Expiry of the allocated timeslot to perform the work stipulated in the permit to work.
Appearance of a risk that has not been covered in the permit to work.
GRP : New requirement

## Slide 15
REQUIREMENT OVERVIEW : Execution
Resuming Activities (Requirement 3.5.6)
Following a suspension of work, the conditions for resuming work are subject to a risk assessment:
If the risk control measures defined in the permit to work remain appropriate, resuming the work is authorised by the issuing authority;
If the risk control measures defined in the permit to work are no longer appropriate, the permit is signed-off and cancelled, and a new permit to work is prepared.
EP, MS and GRP : New requirement
Handover (Requirement 3.5.7)
When a handover concerning entity or affiliate personnel takes place, the permit to work information and management methods are specified in the permit to work procedure.
These include the transfer of the list of permits and their content (at least the description of the work to be performed) and the signature of this list by the incoming issuing authority.
GRP : New requirement

## Slide 16
REQUIREMENT OVERVIEW : End of Work and Permit Closure
End of Work - Closure of the Permit to Work (Requirement 3.6.1)
When the end of work has been confirmed, the corresponding permit to work is closed as per the terms defined in the permit to work procedure.
The provisions for closing the permit to work by the issuing authority includes, as a minimum:
The work site has been restored to a safe and clean condition;
Signature of the end of work (handwritten or electronic) by the performing authority and the permit to work issuing authority;
Withdrawal of the permit to work from the list of permits issued, as well as the associated supporting documentation;
The triggering of the removal of the isolation devices (e.g. spades, blind flanges) and the corresponding tag out devices, provided that all the other permits requiring these isolation devices and tag out devices have also been closed;
Management of long term isolation and inhibition devices or those that are retained beyond the permit to work validity period.
For all high-risk work, the permit is closed based on joint observation by the performing authority and the issuing authority, after the work site has been verified.
Closure of the permit to work does not authorise the start-up of equipment or installations.
RC-MS : For all high-risk work, the permit is closed based on joint observation, after the work site has been verified. New requirement. GRP : New requirement
Organisation of the permit to work process
Preparation
Coordination
Execution
End of work and permit closure
Approval and acceptance
Audits and performance improvement

## Slide 17
REQUIREMENT OVERVIEW : Audits and performance improvement
Audits and Performance Improvement (Requirement 3.7.1)
An audit program within the entity or affiliate is set up to verify that:
The permit to work procedure is applied;
The permit to work instructions are respected.
Performance indicators for the permit to work process are defined and monitored.
These indicators are analysed at a process review at least once a year. The review gives rise to an action plan to improve the process.
EP-RC-MS : The annual process review is a new requirement GRP : New requirement
Organisation of the permit to work process
Preparation
Coordination
Execution
End of work and permit closure
Approval and acceptance
Audits and performance improvement