## Slide 1: Management of Change GROUP HSE RULE (CR-GR-HSE-302)
EXECUTIVE SUMMARY
This rule defines the minimum requirements to ensure that HSE risks are managed when changes are made to assets, operating conditions, procedures, or to an organisation.

## Slide 2
Purpose: HSE requirements for the management of risks related to permanent, temporary or urgent changes made to assets.
This rule completed the requirements of Golden Rule 11.
Scope of Application: All entities and affiliates operating major risk installations:
Low threshold Seveso (whether a regulatory requirement or not);
Offshore oil and gas installations;
Wells and associated installations and pipelines.
Replaces: CR-EP-HSE-022 and CR-RC-HSE-150
    No current MOC rule for the Group, M&S or GRP.
New rule for the M&S and GRP Branches
Contribution: 10% of Process Safety Events result from a failure in MOC as the immediate cause.
REFLEX publication date: 22/07/2019.
Effective date: 6 months following date of publication.

## Slide 3
REQUIREMENT STRUCTURE
Change Assessment
Initial request, justification, documentation recorded with clear objectives.
Change Implementation
Training for personnel, including contractors and suppliers.
Performance review
Periodic evaluation of the MOC Process for compliance with requirements.
Changes are documented and available when the change is conducted.
Impacts are evaluated by relevant disciplines, risk control measures are defined.
Pre-Start Up Safety Review for significant changes.
MOC Process
A MOC process in implemented.
It is described in a procedure (steps, tasks and responsibilities, approval authority, etc.).
A function is designated to coordinate and track all change requests.

## Slide 4
REQUIREMENT OVERVIEW: MOC Process
MOC Process MOC (Requirement 3.1.1)
A process is set up to manage permanent, temporary or urgent changes that present potential impacts on HSE risk level and concern:
Assets (e.g. equipment, process, technologies, materials, safety thresholds/parameters);
Operating conditions and operating procedures;
Operating personnel and organisation.
A function is designated to coordinate and track all change requests of the entity or affiliate.
Comments
E&P: The function of MOC Coordinator is not specifically required in the existing rule.
R&C: Organisational changes are now part of the scope for this new rule.

## Slide 5
REQUIREMENT OVERVIEW: MOC Process
MOC Procedure Minimum Content (Requirement 3.1.2)
The entity describes the MOC process in a procedure that addresses as a minimum:
The MOC process coordination;
The change approval process steps (planning, coordination, control, etc.);
The list of typical changes subject to a MOC process, as well as replacements-in-kind not covered by this process;
The tasks and responsibilities of each party involved in the MOC process (e.g. originator, evaluation team members, approval authority, Pre-Start Up Safety Review [PSSR] leader);
Training required for the implementation of the process;
The MOC process assessment.
Comments:
E&P: Requirement to write a procedure.
R&C: Minimum content of the procedure to be followed.

## Slide 6
REQUIREMENT OVERVIEW: Change Assessment
Change Initiation (Requirement 3.2.1)
The change request, including its justification, is formally recorded and documented so that the objectives of the change:
Remain clear during its evaluation and implementation phases;
Are communicated to relevant parties;
Are traceable after the change has been made
No change
Change Evaluation Including Risks and Impacts Assessment (Requirement 3.2.2)
The evaluation of the change includes an assessment of the HSE risks and potential impacts of the change. This evaluation involves:
The function in charge of HSE aspects as well as representatives of relevant disciplines depending on the nature of the change (e.g. inspection, maintenance, operations, engineering);
Other parties impacted or influenced by the change;
Identification of relevant regulations, standards and applicable REX
The impacts and HSE risks are mitigated by the defined risk control measures, as necessary.
No change

## Slide 7
REQUIREMENT OVERVIEW: Change Implementation
Training and Communication (Requirement 3.3.1)
As required, training for personnel (including contractors and suppliers) impacted by the change is defined, planned and organised ahead of the change.
External stakeholders and potentially affected personnel are notified of the change and of the associated risk management measures.
No change
Documentation Update (Requirement 3.3.2)
All documents impacted by the change are updated and made available as soon as the change is conducted.
No change
Pre-Start Up Safety Review (Requirement 3.3.3)
Before restarting a physically modified installation after a significant change, a Pre-Start Up Safety Review (PSSR) is carried out.
All the documents required for the start-up are made available for the PSSR.
Comment
E&P: New Requirement (but currently covered in EXP practices).
R&C: The concepts of receipt and start-up permit to be included in the site procedure already exist; start-up review becomes a requirement integrated into the process.

## Slide 8
REQUIREMENT OVERVIEW: Performance Review
MOC Process Assessment (Requirement 3.4.1)
Performance of MOC process is periodically assessed.
New Requirement
New requirements for all Branches.