## Slide 1: Temporary Sealing Systems
Company Rule – CR-GR-HSE-426
This rule sets out the minimum HSE requirements to be met when preparing, installing, registering and monitoring Temporary Sealing Systems (TSS).
Notes: Afin de respecter la dénomination de la Marque, merci de veiller à la bonne orthographe de TotalEnergies.
TotalEnergies s’écrit en un seul mot, sans espace, avec un « s » à la fin, avec le T et le E en majuscules, les autres lettres en minuscules, et pas d’accent sur le E majuscule.
Elle s’écrit bien TotalEnergies et non :
Total Energies (avec un espace)
totalenergies
total energies
Totalenergies
Total energies
totalEnergies
total Energies
TOTALENERGIES
TOTAL ENERGIES

## Slide 2: CR-GR-HSE-426
 | Context | Safety of technicians (Antwerp REX) when using Temporary Sealing System (TSS) and integrity of the temporary repair (other REX). Extend REG-GR-SEC-024 MAJOR REX from clamps to any kind of temporary sealing systems
 | Object | HSE Requirements for Temporary Sealing Systems (TSS) Rewriting from REG-GR-SEC standard to new CR-GR HSE standard
 | Scope | All TSS including, but not limited to Mechanical clamps with sealant injection for equipment piping, flanges, piping Composite repair systems for equipment piping and piping Collars on piping (standard commercial bolted systems) All Businesses of the Company
 | Exclusions | Weld repairs.
 | Replace | 1 rule (REG-GR-SEC-024). Impact on CR-MS-HSEQ 202 (Operations and works at risk § 7. temporary leak repair)
 | Dates | Application : 6 month after validation/publication

## Slide 3: Extension of scope with same requirements on clamp
Clamp with injected sealant for equipment pipes, flanges and pipes
Composite repair systems for equipments pipes and pipes
Collars on piping (standard commercial bolted systems)
REG-GR-SEC-024
CR-GR-HSE-426

## Slide 4: Rule Structure : 10 themes, 16 requirements
1
Process Organization
2
Prerequisite for TSS*
3
  External risk analysis
6
7
  Installing TSS*
  Preparation of permanent repair
4
Internal risk analysis
5
  Intervention decision
8
9
10
  Online monitoring TSS*
TSS* removal
Internal audit process
16 Requirements
1- Procedure, 2- Approved company and authorized staff
3- Prerequisite for the installation of a TSS
4- Compiling the intervention dossier , 5- Technical feasibility study and choice , 6- Preliminary risk analysis
7- External risk analysis, 8- External company Dossier
9-Intervention Decision
10- Identification, registration, 11- Work acceptance
12- Preparation and scheduling of the permanent repairs
13- Monitoring in operation, 14 Additional intervention for a TSS
15- Expertise during removal
16- Internal audit
* TSS : Temporary Sealing System

## Slide 5: Summary of requirement improvements
16 Requirements
1- Procedure, 2- Approved company and authorized staff
3- Prerequisite for the installation of a TSS
4- Compiling the intervention dossier , 5- Technical feasibility study and choice , 6- Preliminary risk analysis
7- External risk analysis, 8- External company Dossier
9- Intervention Decision
10- Identification, registration, 11- Work acceptance
12- Preparation and scheduling of the permanent repairs
13- Monitoring in operation, 14- Additional intervention for a TSS
15- Expertise during removal
16- Internal audit
* TSS : Temporary Sealing System
Modifications versus REG-SEC-024
No change but scope extension
No change but scope extension
Integration of recent REX learnings in Appendix 1, Choice of TSS type added due to scope extension Need to differentiate composite repair and bolted system for isolated equipment
Need to differentiate composite repair and bolted system for isolated equipment No change but scope extension
No change but scope extension
Unique reference added and details of register No change but scope extension
No change but scope extension
No change but scope extension No change but scope extension
Required now only in case of issues for example due to sealings problems or when the corrosion mechanism is not well established
New requirement

## Slide 6: Modification for branches and added value
RC : limited impact due to existing CR (CR-RC-MIT 009).
  Each site has already a procedure . Needs to be updated.
  Added value : some improvement and recent REX integrated
EP : several technical GS covering composite repair but no CR.
  Processus needs to be formalized
  Added value : Today no specific HSE rules but different technical GS on the topic with some gaps. Benefit from lessons learnt coming from recent REX mainly from RC
GRP : limited impact Added value : REX mainly from RC
MS : limited impact due to existing CR (CR-MS-HSEQ 202)
  Added value : REX mainly from RC

## Slide 7: Thanks

## Slide 8: Annexes

## Slide 9: Requirements
No change (already in REG-GR-SEC-024) but scope extension
{Requirement 3.1.1: Temporary Sealing Systems procedure
The process for temporary sealing systems is set out in a documented procedure incorporating at least the requirements of this rule. It specifies the roles and responsibilities and the approval levels for each step in the process based on the risks.
{Requirement 3.1.2: Approved company and authorized staff
Only contractors selected and approved in advance by the entity or subsidiary for this type of intervention are retained. The contractor provides the entity or subsidiary with a list of qualified intervention staff.
No change (already in REG-GR-SEC-024) but scope extension

## Slide 10: Requirements
Step already in REG-GR-SEC-024 but scope extension
No change (already in REG-GR-SEC-024). Integration of recent REX learnings in Appendix 1
Requirement 3.2.1: Prerequisite for the installation of a temporary sealing system
Permanent repair, preferred to the installation of a temporary sealing system, has been considered and evaluated. In most cases, the installation of a temporary sealing system entails high risks, so it is deemed exceptional and subject to special measures. If installation of temporary sealing system is necessary, it will be initiated only when following conditions have been checked: The repair area is sufficiently accessible and can be easily evacuated, making it safe for an intervention. The risks of auto-ignition, flammability, explosion in contact with a hot point, toxicity and/or burning, pollution and mechanical damage around the leak are acceptable with the implementation of risk control measures.
Requirement 3.3.1: Compiling the intervention dossier
The entity or subsidiary gathers all necessary information and prepares the intervention dossier for the installation of the temporary sealing system. The minimum contents of this dossier are stated in Appendix 1.

## Slide 11: Requirements
Technical feasibility already in REG-GR-SEC-024. Choice of TSS type added due to scope extension
Step already in REG-GR-SEC-024. Need to differentiate for composite repair and commercial bolted system on isolated equipment for simplification (pilot feedback)
Requirement 3.3.2: Technical feasibility study and choice of temporary sealing system type
The entity or subsidiary studies the technical feasibility of installing the temporary sealing system and decides on the most appropriate type of temporary sealing system. This choice is based on the applicable regulations, guides and technical specifications taking account of the damage mechanism, as well as the product type, the operating conditions and the required service life of the equipment.
Requirement 3.3.3: Preliminary risk analysis
A preliminary risk analysis based on the checklist in appendix 1 is formalized and validated by a multidisciplinary team. Based on this analysis the decision can be taken on whether to conduct the temporary sealing system study. For composite repair systems or commercial bolted systems installed on isolated equipment risk analysis can be realized during dedicated job risk analysis of permit to work on basis of typical risk analysis per type of service

## Slide 12: Requirements
Requirement 3.3.4: Risk analysis and acceptance by the external company
The entity or subsidiary asks the contractor to conduct its own risk analysis based on the intervention dossier, the results of its investigations on site (site visit and discussion with at least the person in charge of the dossier) and the conclusions of its feasibility studies. The result of the risk analysis by the contractor determines whether it accepts the contract to install the temporary sealing system. This requirement is not mandatory for composite repair systems or commercial bolted system installed on isolated equipment
Requirement 3.3.5: External company dossier
If it accepts the contract, the contractor is asked to provide a preparatory dossier including at least the points stated in Appendix 2.
}
No change (already in REG-GR-SEC-024)
No change (already in REG-GR-SEC-024). Need to differentiate for composite repair and commercial bolted system on isolated equipment for simplification (pilot feedback)

## Slide 13: Requirements
Already in REG-GR-SEC-024. Unique reference added and details of register (Antwerp REX post accident). No requirements on permit to work already in CR-GR-HSE-402 (permit to work) .Repair by clamp defined as high-risk activity if done online
Requirement 3.4.1: Intervention decision
The intervention decision is based on the (internal and external) risk analyses and formally approved by the signing of the intervention dossier by the persons in charge as designated in the temporary sealing system procedure at the entity or the subsidiary and by the contractor.
l
No change (already in REG-GR-SEC-024)
Requirement 3.5.1: Identification, registration and monitoring
A unique temporary sealing system reference number is affixed to the temporary sealing system in the field and on the plan. Every temporary sealing system installation or additional intervention must be recorded and tracked in accordance with the arrangements set out in the procedure of the entity or subsidiary. A comprehensive register for monitoring temporary sealing systems is available on site. This comprises of: - the unique reference for each temporary sealing system - the temporary sealing system type - the date on which it was taken into service - the dates of any additional interventions - the scheduled and actual completion date of removal of the temporary sealing system
}

## Slide 14: Requirements
Requirement 3.5.2: Acceptance of work
An intervention report must be drawn up by the contractor (see appendix 2) and the entity or subsidiary, after work is completed and formally accepted on the site of work. These reports are grouped together in the intervention dossier.
}
No change (already in REG-GR-SEC-024)
No change (already in REG-GR-SEC-024)
Requirement 3.6.1: Preparation and scheduling of the permanent repairs
Alongside the installation of the temporary sealing systems, the preparations are started to ensure that the necessary equipment is available for the permanent repair. The permanent repair should be done at the earliest opportunity (scheduled shutdown or turnaround or unscheduled shutdown where the equipment is cleared for maintenance) after the installation of the temporary sealing systems without exceeding the initial deadline as set.

## Slide 15: Requirements
Requirement 3.7.1: Monitoring in operation
The specific monitoring arrangements (operator round, inspections, detectors, specific process conditions etc.) are implemented by the competent entities of the site, as set out in the procedure of the entity or subsidiary.
No change (already in REG-GR-SEC-024)
No change (already in REG-GR-SEC-024)
Requirement 3.7.2: Additional intervention for a temporary sealing system
The reasons for the additional intervention must be identified, and the number of additional interventions already completed taken into account along with how the leak flow rate is changing. A new risk analysis is conducted as set out in appendix 1. Furthermore, in case of mechanical clamps with sealant injection, after three reinjections, every subsequent reinjection must be formally approved by the management of the entity or subsidiary.

## Slide 16: Requirements
New requirement
Requirement 3.8.1: Expertise during removal
When a temporary sealing system is removed, in case of sealing difficulties or when corrosion mechanism is not well established, the equipment and surrounding area are visually inspected in the presence of the designated representatives of the entity or subsidiary operating the site to make observations on the damage mechanism of the equipment and the condition of the temporary sealing system.
}
Requirement already in REG-GR-SEC-024. Required now only in case of issue
Requirement 3.9.1: Temporary sealing systems internal process audit
An audit programme is set up at the entity or subsidiary to verify the application of the temporary sealing systems procedure. At the end of the audit, an action plan is issued and the implementation is checked in periodical reviews until all instances of non-compliance have been dealt with appropriately.

## Slide 17: Documents used
Branche |  | Référence |  | Titre
Groupe |  | REG-GR-SEC-024 |  | REX MAJOR REX Requirements for sealing leaks online
E&P |  | GS-EP-PLR-310 GS-EP-PVV-711 GS-EP-EXP-311 GM-EP-COR-054 |  | Pipeline composite repair systems – wet tape systems according to ISO24817 Composite repairs for metallic pipeworks and pressure vessels Plant integrity –Minimum inspections requirements (4.5.2.6 temporary repairs) Corrosion (10.1 Composite temporary repairs)
M&S |  | CR MS HSEQ 202 |  | High-risk operations and works (§ 7. Temporary sealing of leaks)
R&C |  | CR RC MIT 009 GM-RC-MIT 520 GM-RC-MIT-225 |  | Management of temporary leak repair systems. (rule co-signed by HSE) Guide for the Design and Manufacture of mechanical clamps for on line repair Accreditation of contracting companies in charge of on-line leak sealing works
GRP |  |  |  | 
Notes: Click to add text

## Slide 18: WORKING GROUP
Domain Owner (DO) : Pol HOORELBEKE
Technical Authority (TA) : Eric VERDONCK
  Participants:
  C. Champigny HSE/MMR/REF
  H. Rodriguez EP/DSO/IP/EXP/MIN/INS
  J. Donadey RC/IND/EXM/EXP
  J. Negre HSE/EP/SHI/ASSD
  L. Cristini MS/SMR/SLP/TP/BE/TEC
Main contributors during reviews : Antwerp refinery
TEP Angola
TEP Congo
US RC Sites
Company TEAM
RC/IND/EXM F. CLEMENT
EP/DSO/IP/TEC/PVV I. BOUGET
Notes: Click to add text

## Slide 19: Avertissement - Propriété intellectuelle
Définition TotalEnergies / Compagnie
Les entités dans lesquelles TotalEnergies SE détient directement ou indirectement une participation sont des personnes morales distinctes et autonomes. Les termes « TotalEnergies », « compagnie TotalEnergies » et « Compagnie » qui figurent dans ce document sont génériques et utilisés à des fins de convenance pour désigner TotalEnergies SE et les entités comprises dans le périmètre de consolidation. De même, les termes « nous », « nos », « notre » peuvent également être utilisés pour faire référence à ces entités ou à leurs collaborateurs.
Avertissement
Cette présentation peut contenir des déclarations prospectives, au sens du Private Securities Litigation Reform Act de 1995, relatives à la situation financière, aux résultats d'exploitation, aux activités, à la stratégie et aux projets de TotalEnergies, qui sont soumis à des facteurs de risque et à des incertitudes résultant de changements dans, notamment, le développement et l'innovation technologiques, les sources d'approvisionnement, le cadre juridique, les conditions de marché, les événements politiques ou économiques. TotalEnergies n'assume aucune obligation de mettre à jour publiquement les déclarations prospectives, que ce soit en raison de nouvelles informations, d'événements futurs ou autres. De plus amples informations sur les facteurs susceptibles d'affecter les résultats financiers de la Compagnie sont fournies dans les documents déposés par TotalEnergies auprès de l'Autorité des Marchés Financiers et de la US Securities and Exchange Commission. En conséquence, aucune certitude ne doit être accordée à l'exactitude ou à la justesse de ces déclarations.
Propriété intellectuelle
Toute reproduction, publication, transmission ou plus généralement toute exploitation des éléments de cette présentation est interdite, sauf autorisation écrite expresse de TotalEnergies.