## Slide 1: World Day for Safety April 22, 2024
Manager Kit V2*
* update slide 11

## Slide 2: Agenda
Introduction
Knowing the major accidents and what they have changed for the Company
Return of experience, how does it work and what are the main benefits?
How to well manage the REX in your affiliate / site?
Organizing the WDfS
How to organize the exchange workshop?

## Slide 3: Introduction
01.

## Slide 4: Introduction
On April 22, the Company will celebrate the 17th edition of World Day for Safety (WDfS). Following on from the 2023 edition on major technological risks, we will be gathering around the theme "Major Accidents and REX". This year, TotalEnergies is celebrating its 100th anniversary: a century of challenges and technological progress, but also a century of improvements in terms of safety at the workplace and in our facilities. The Company has learned from its major accidents and those of the Industry. It has learned from this and has implemented an events management and a ‘return of experience’ process to advance the safety of its operations. At the same time, Safety is implemented daily in all our activities by the employees of TotalEnergies and contractors with a common objective of "Zero fatal accidents".

## Slide 5: However…
...recent accidents remind us that major accidents can still occur in the industry.
Conakry, Guinea, December 2023
Explosion at an oil tank farm
Beirut Port, August 2020
Ammonium nitrate storage explosion
We need to be aware of these risks, to know them better to control and prevent them!

## Slide 6: Main objectives of the WDfS
WDfS 2024 will therefore be an opportunity, for you, your teams and partners:
  To remember some major accidents of the past. To discuss about the lessons learned from them. To see, through our REX process, how we should continue to learn and progress by learning lessons from more recent serious incidents, wherever they may have occurred.
On the day of the WDfS, a video by Pol Hoorelbeke, VP Major Risks Division,
will remind us of these objectives. Share it during all your different animations!
You will find out this video in the HSE Toolbox.

## Slide 7: Knowing the major accidents and what they have changed for the Company
02.

## Slide 8: Sharing awareness of the most important risks helps develop a strong Safety Culture
The activity of an organization can generate different types of accidents.
These events are not in the same way in terms of probability and severity.
  The challenge is to maintain vigilance and management
  of the most significant risks related to site activities: i.e. those related to fatal accidents and major technological
  accidents. They occur least often (so they are less visible)
  but they threat the personnel and the organization,
  see GM-GR-HSE-351 - link
  An organization maintains a robust
  Safety Culture when all the players share
  and discuss their perceptions of
  the most significant risks.
Only humans have memory. Let's share our knowledge of the most important accidents!
Major
accidents
Fatal
accidents
Relatively minor accidents at workplace
What is threatening the most the organization?
Severity
Probability

## Slide 9: Let's share 9 accidents that have marked the history of the Industry and of the Company
The Branches have selected 9 “historic” accidents of our industry or of the Company which are printed in our collective mind.
These incidents have been specifically chosen because they have led, through their analysis, to modify and improve our ways of operating and therefore to enhance the safety of our operations.
In this Manager Kit, each accident is summarized on a slide.
In addition to that, an additional media (PPT or video) will be provided in the HSE Toolbox for further explanation.
We recommend that you use these media as part of your workshops to discuss these accidents and their lessons for the Company with all the participants.

## Slide 10
2005 - Buncefield (MS)
2010 - Deepwater Horizon (EP)
1988 - Piper Alpha (EP)
1999 - Erika (TS)
2001 - Teeside Enron (GRP)
2013 - Ooltgensplaat Fire (GRP)
2017 - Qapco (RC)
2018 - Mostorod (MS)
2019 - Normandie (RC)

## Slide 11: 1988 Piper Alpha Platform destruction (EP) UK North Sea, 167 fatalities, 3.4 Billion USD
Summary of the facts
The inquiry into the Piper Alpha disaster (July 6, 1988) concluded that the most likely cause of the initial explosion was the release of as little of 30kg of condensate through an unsecured blind flange where a pressure safety relief valve (PSV) had been removed as part of maintenance on a standby condensate pump. The shift night operators were not aware the PSV had been removed on the previous shift when putting the pump back into service.
The initial explosion knocked down firewalls leading to escalation to other parts of the platform including the loss of the Control Room (CR) and critical safety systems. The majority of the crew mustered in the Living Quarters (LQ). 50 mins after the initial release, the 1st gas riser ruptured followed shortly after by the rupture of the other oil and gas risers and the eventual destruction of the platform.
The deluge system was never activated due to automatic start being on long term inhibit due to diving activities. There was smoke ingress to accommodation module and the lifeboats were not launched due to the route to them being blocked by smoke and flames.
The majority of those who died suffocated due to carbon monoxide and smoke ingress into LQ. The 61 persons who survived did so by jumping into the sea.
Causes
PERMIT-TO-WORK SYSTEM - Failures in system
SHIFT-HANDOVER – No formal handover between shifts with CR Operators unaware the PSV had been removed
SAFETY CULTURE – Culture of production over safety.
MANAGEMENT OF CHANGE (MoC) – Hazards from new gas processing equipment & gas risers not assessed e.g. firewall failure following explosion.
FIREWATER PUMPS – Inhibition of automatic start-up.
PIPELINE ISOLATION – Flow from surrounding platforms continued to be pumped into Piper Alpha.
SAFETY SYSTEMS – Not designed to survive fire and explosion events
ENERGENCY RESPONSE – Lack of training, drills or exercises.
How has this accident changed the safety of our operations?
The disaster had a significant impact on how we design, maintain and operate our facilities and led to design and operational improvements on our existing facilities and modifications to our referential for future projects such as:
MAJOR HAZARDS – Demonstrate all major hazards have been identified and are mitigated through Technological Risk Assessment (TRA) studies including brownfield changes (MoC) e.g. fire and explosion studies, Temporary Refuge impairment study.
SAFETY CRITICAL EQUIPMENT/BARRIERS – are identified, have redundancy, and are maintained so they are available during an incident.
PIPELINE ISOLATION – Provision of Subsea Isolation Valves (SSIV).
ESCAPE, EVACUATION & RESCUE – Provision of smoke hoods, method to escape to sea, freefall lifeboats, standby vessels, drills.
OPERATIONAL INTEGRITY – Major improvements in Permit-to-Work, Shift Handover, Lockout /Tagout and Downgraded Situation management.
MAJOR ACCIDENT MANAGEMENT – New position of RSES (Safety and operation management) defined. Emergency management training for RSES and Deputy and reinforced need for drills and exercises.
SEE ALSO THE NEW VIDEO DEVELOPPED BY EP TEAMS
Notes: For WdfS2024, the EP Branch has created a special video on the Piper Alpha accident, that as changed the way to design and operate offshore platforms

## Slide 12: 1999 Sinking of the Erika (Trading-Shipping) Atlantic Ocean. Over 10,000 m3 heavy fuel oil at sea, 400 km coastline soiled, several thousand birds oiled
Summary of the facts
The tanker chartered by Total sank on 12 December 1999 off the French Brittany coast. Sailing from Dunkirk to Livorno, the ship has been caught in a storm. Its internal structures crumbled, the hull tore in the middle parts, and it broke in two, spilling part of its 37,000 tons of heavy fuel oil. The crew of 26 seamen was winched out by a naval helicopter, all unharmed.
Direct causes
Corrosion, structural stresses and fatigue.
Indirect causes
Lack of maintenance and control- verification – deficient surveys.
Faulty ship-operator management.
How has this accident changed the safety of our operations?
Regulatory:
Renewal of the world fleet for double hull tankers. Accelerated phasing-out of single hull tankers.
Enhanced surveys of vessel’s hull and structures.
Internally:
Strengthened organization of the Shipping Division. Reinforcement of vetting.
For the Industry:
Pooling of Tanker Inspection Reports (OCIMF). Harmonization of the Classification Societies rules on vessel hull strength and construction (CSR).
SEE IN THE HSE TOOLBOX THE TESTIMONIAL VIDEO CREATED FOR THE WDfS 2024

## Slide 13: 2001 Explosion on Teesside CCGT ENRON (GRP) England - Wilton (5% of the national electricity production) - 3 fatalities (burned beyond recognition)
Summary of the facts
Necessity to shutdown the transformer to allow essential maintenance (5 years inspection).​
Staff realized that power levels were too high to allow a straightforward shutdown
=> they agreed to carry out a "tap change“ (working while the power was reduced but still on). ​
The work to "tap" the transformer led rapidly to the explosion.
Similar events
Cartagena/Colombie/1999: 4 FAT
Spencer/USA/2000: 2 FAT
Causes
The transformer has submitted a defect and an overheat leading oil inside it to boil and then to a blast.
What are the key points of this incident?
Avoid working on an operating electrical equipment.
Anticipate the different tasks to be performed.
Stipulate mitigation measures to cover the risks identified in the Permit to Work process.

## Slide 14: 2005 Explosions at the Buncefield Depot (MS) 43 minor injuries, 2,000 evacuees, plume of smoke within a radius of 100km, significant impact on the local community
Summary of the facts
On 11th of December 2005, three explosions hit the Buncefield oil terminal, approximately 40 km from London. The explosions were caused by the overfilling of a fuel tank, resulting in flammable liquid in the retention bund.
A large vapor cloud then formed which found an ignition source and subsequently ignited resulting in various explosions and a large-scale fire.
The resulting fire destroyed 20 storage tanks and lasted 5 days destroying most of the facility and damaging surrounding homes and business premises. Fortunately, there were no fatalities but 43 people were injured and approximately 2000 people had to be evacuated from the surrounding area.
The fire also caused environmental pollution, including air pollution and water pollution because of run off fire water mixed with product entering the water system. The Buncefield fire was the largest industrial fire in peace time Europe.
The cost of the disaster ran into billions with clean up costs, fines, rebuild costs and litigation along with significant impact on the environment and local community.
Causes
The investigation revealed that although the tank was fitted with physical controls including high level alarms, auto cut offs and sprinkler system, these systems did not function properly due to design and maintenance issues, this allowed the spill to occur and the vapor cloud to form, which ultimately resulted in the explosion. Other issues around shift handover also resulted in confusion in relation to the tank filling status via the external fuel lines.
What has this accident changed in the safety of our operations?
Updating of design standards and operating methods, in accordance with regulations (overflow prevention).
For all products with a flash point below 37.8°C in large storage tanks:
Equipment for tanks and their retentions: level sensors with alarms, servo valves for automatic cut off, hydrocarbon detection in bunds, Bund integrity and retention.
Updating of operating methods: operational instruction of tank farm operations, monitoring of the integrity of installations, emergency response.
It should be noted that these lessons have also been considered by the RC Branch for all hydrocarbon storage tanks
SEE IN THE HSE TOOLBOX THE TESTIMONIAL VIDEO CREATED FOR THE WDfS 2024
MAJOR REX

## Slide 15: 2010 Deepwater Horizon disaster (EP) US Gulf of Mexico, 11 deaths, 5 million barrels of crude oil spill & 1000km of coast polluted
Summary of the facts
On April 20, 2010 uncontrolled release of oil and gas (“blowout”) occurred at the Macondo oil well – operated by BP - during a temporary well abandonment operation which involved isolating the reservoir with casing & cement.
The loss of control was caused by the failure of that deep barrier, not properly installed and tested.
The escaping hydrocarbons found an ignition source on the Deepwater Horizon drilling rig and caused an explosion.
11 people died, 17 were injured and 115 people were evacuated. The drilling rig sank within 36 hours of the initial explosion.
It took 87 days to stop the oil spill. Nearly 5 million barrels of oil were released, causing massive marine and coastal damage.
BP paid around $65 billion to recover a safe situation, clean-up costs and legal fees linked to the largest environmental disaster in U.S.
Causes
Well integrity was not established Primary and Secondary Barriers failed.
Hydrocarbon entered the well undetected.
Blowout preventer did not seal the well.
Hydrocarbon ignited on the rig deepwater horizon.
What has this accident changed in the safety of our operations?
This event is a step-change in the drilling and wells industry. Beyond the fatalities and the environmental impact, the O&G companies realized how they could be vulnerable to this type of accident.
In a nutshell, the actions were around:
PEOPLE: Developed a blowout prevention culture within operational population. Improved reporting and shared events, enhanced training contents and developed on human factors aspects, formalized chain of commands, roles & responsibilities.
PROCEDURES: Revisited majority of referential. Improved well control and emergency response readiness. Perform Technological Risk Assessment (TRA).
EQUIPMENT: Developed well response equipment dispatched worldwide. Audit safety critical equipment. Monitor operation with Real Time Support Center and Digital tools.
SEE IN THE HSE TOOLBOX THE TESTIMONIAL VIDEO

## Slide 16: 2013 Ooltgensplaat Windmill Fire (GRP) Netherlands – 2 fatalities
Summary of the facts
Deltawind’s Piet de Wit wind farm – first fatal accident due to a wind turbine fire.
Repairs were carried out in the nacelle by 4 technicians.​
A fire started in the afternoon, but it took until evening for a special team of firefighters to arrive and ascend with a large crane.
Only 2 mechanics managed to evacuate.
One fell to his death from the full height.
One died from burns inside the nacelle.
Causes
Electrical short-circuit.
Dangerous phenomenon
Blast, fire.
What has this accident changed in the safety of our operations?
Focus on inherently safe design to reduce risk of fire: electrical architecture design.
Focus on improved design for safety: safety venting, escape routes.
Evolve O&M philosophy towards more automation. For example:
    Condition Monitoring System to determine the optimum point between corrective and scheduled maintenance through vibration/acoustic-controlled O&M techniques for the wind turbine and optical strain gauges for the blades.
    IoT : Mobile Video Supportive System (MVSS), to send the information and direct the operator at the site location to selectively perform necessary operations.
    Utilization of drones to perform inspection.
  Global industry rethinking of operator training, focusing on the enclosed environment (development of immersive training).
  Escape / Evacuation philosophy and associated operational procedure (to ensure safe evacuation), including specific training of firefighters and rethinking of fire-fighting techniques.
  Rope based descent (RBD) Emergency Evacuation System.

## Slide 17: 2017 Fire and fall of the flare in Qapco (RC) Qatar, business interruption
Summary of the facts
On 06/01/2017 during a start-up phase of the steam cracker, an excessive amount of liquid ethane/ethylene was sent to the flare network. The capacity of the heater does not allow the entire liquid to be vaporized. The ethane / ethylene expansion generates a very low temperature (-100°C approximately), which weakens the steel and generates a loss of containment with cloud ignition. The torch was impacted by the fire and eventually broke.
Causes
  Excessive drainage of liquid to the flare network. Poorly assessed and unrecognized risk (training). High Level Alarm failure on flare drum. No low temperature alarm.
What has this accident changed in the safety of our operations?
Each RC site has dealt with this REX and has put in place, if necessary, additional measures to better control the risk, which are regularly monitored by the branch management.
The action plan includes:
Setting up redundant high-level alarms on flare drums (and low temperature alarm for LPGs).
Training/sensitization of operators on the risk of poorly controlled sending of liquid to a flare network. Identification of risky situations.

## Slide 18: 2018 Explosion in a tank in Mostorod (MS) Two deaths, two seriously injured, two hospitalizations
Summary of the facts
On the morning of 4th October 2018, contractors were completing work on a gasoline storage tank (TK08) when an explosion occurred which caused the tank roof to be blown off and land on the loading station some 40 meters away!
The accident resulted in the death of 2 workers and injured 4 others.
All operations were stopped at the depot.
The depot's Internal Operation Plan was triggered, along with the subsidiary's Crisis Management Unit (CMC) to manage the event and coordinate with the local emergency teams (fire/ambulance) and the Headquarters Crisis Unit.
Causes
Human: lack of understanding of the work permit, non-compliance with return to service phases, lack of knowledge of the dangers related to gasoline.
Organizational: poor planning (the vent cover grille should have been welded to the floor before reinstallation), poor instructions, permits issued without suitable checks and inspections on field.
Technical: Isolation inside the tank 8 and removed before hot work completed, allowing flammable vapors inside tank 8.
What has this accident changed in the safety of our operations?
Hot work, work inside the tank:
Work permit / hot work with proper risk analysis and continual atmosphere explosivity monitoring.
Isolation procedure including isolation scheme and isolation identifications (tags).
Isolation by physical disconnection, spool removal for example as close to the vessel as possible.
Hand back procedures with checks (punch out).
Start-up checklists before putting back in service.
MAJOR REX

## Slide 19: 2019 Normandie – D11 fire (RC) Significant damage (50x50m area on 3 levels), unavailability of the unit for 19 months, no injury, no environmental consequence
Causes
Undetected corrosion on a gas line. Lack of permanent display of fire and gas alarms in the control room. Lack of visibility of the watering resources.
What has this accident changed in the safety of our operations?
Each RC site has dealt with this REX and has put in place, if necessary, additional measures to better control the risk, which are regularly monitored by the branch management.
The action plan includes, inter alia:
Inspect line supports (trunnions) and replace if corrosion is found.
Guarantee a permanent display of "Fire & Gas" alarms in the control room and training of panels to avoid masking/filtering of Fire & Gas alarms.
Match water needs with available resources (fixed and mobile) for each major fire scenario.
Summary of the facts
On Saturday 14th of December 2019 :
Leak on a 3'' (3 inch) diameter gas line, expansion of a pool and ignition of the cloud with flames 50m high. Destruction of a part of the D11 unit (50mX50m). Late detection of the vapor clou.d Ineffectiveness of firefighting equipment at first.
MAJOR REX

## Slide 20: Learning from accidents so that they don't happen again: that’s the goal of return of experience
Following these historic accidents, the Industry and the Company have implemented procedures for analyzing HSE occurrences (anomalies, near-misses or accidents) to determine the facts, consequences and causes.
From that, lessons were learned, recommendations were made and implemented to prevent that this accident happen again.
This is called the Return of experience (REX) that we will see in the next part of the Manager Kit.

## Slide 21: Return of experience, how does it work and what are the main benefits?
03.

## Slide 22: Return of experience is a learning process for continuous improvement
Based on an occurrence on field (anomaly, accident, good practice), Return of experience (REX) generates a continuous improvement of know-how, making possible to move from a sharing culture to a learning culture, to always progress together.
Knowledge of Return of experience also promotes the learning and understanding of the rules.
The REX has a memory function by gathering the knowledge acquired and making it available to the teams.
ACT
PLAN
DO
CHECK
Anomaly, accident, good practice
Corrective Action

## Slide 23: How does the return of experience work?
The return of experience is based on the steps below
If the lessons learned from an accident are rigorously implemented, the same accident cannot happen again.
Reporting the HSE incident
Gathering information
about the HSE incident
Analysis
of the HSE
incident
Sharing
information
with the right
people
Implemen-tation and follow-up of recommend-dations
The implementation of recommendations is then fundamental

## Slide 24: The REX benefits
Avoiding
further accidents
Improving our
standards and making
it easier to learn
the rules
Advancing
good practices
Remembering
accidents and lessons
learned to use them daily

## Slide 25: Avoiding further accidents Example: consideration of the D11 REX in Myanmar
Following the D11 accident at the Normandy refinery in December 2019, sites were asked to list, inspect the trunnions (unused piping arms) and replace them if necessary.
During the general inspection conducted at a site in Myanmar:
  Out of 70 trunnions identified and inspected, 2 were found to be severely corroded.
  One of the trunnions was on a 2'' (105 bar / 43°C) high-pressure gas line which, if leaked, could have had serious consequences.
  The trunnion was replaced immediately. A bracket was repaired by a temporary modification without production shutdown.
Rigorous application of the REX prevented a potentially significant accident All together, daily, let's be rigorous in the implementation of the REX!
25

## Slide 26
Accident
Awareness kit
HSE Major REX sheet
Major REX video
Improving our standards and making it easier to assimilate the rules
Example of the Mostorod accident follow-up
Mostorod
Risks awareness
of works on tanks
Analysis /
information / training
 Evolution of company rules, audits
Database fortification

## Slide 27
MyREX Database
(access link)
The digital application
Remembering accidents and lessons learned to use them daily
Risk Advisor
(coming soon)
Using AI, Risk Advisor indicates
which REX to look at specifically
to establish a work permit
The REX is our memory, and most of the accidents’ causes have already been identified.
You should use them daily to share about it, to prepare your risk analysis, your shutdowns, your projects, your training, etc.
Toolbox is a public REX database, which
was built with other Oil & Gas majors.
Internet url : https://toolbox.energyinst.org/
And a good REX
search engine:
World Day for Safety 2024 – Manager Kit
27
Notes: MyREX contains more than 2,000 REX documents. You'll find the 4 types of HSE REX (major REX, REX, Safety Alert and good practice), REX document templates, videos (including major REX), external REX and links to various REX databases.
REX can also be accessed via Tapir, in addition to the applicable standards and rules.
Toolbox has been developed by various Oil&Gas companies and offers anonymised REX that is very easy to share, both internally and with contractors. 10 languages are available. On a smartphone, you can use the website to create a shortcut on the phone's home screen.
Do not confuse Toolbox, which is a public, anonymous, multi-company tool, with Toolbox HSE, a TotalEnergies' internal REX-sharing platform.

## Slide 28: Advancing good practices
The REX also provides an opportunity to learn from successes and disseminate good practices
The Safety+ tool and any other approach to recognizing good practices can be a source of REX.
As such, the Company has the “HSE Good practice” format to formalize the teaching of good practices.
To be used to advance
good practices

## Slide 29: How to well manage the REX in your affiliate / site?
04

## Slide 30: TotalEnergies' REX process is organized in Corex
TotalEnergies has set up an organization based on 3 REX committees (“HSE Corex”) that interact with each other.
In addition, the CODIR HSE follows up the implementation of the recommendations of certain REX such as the Major REX.
Local
HSE
Corex
Interbranch
Company HSE
Corex
CODIR
HSE
Branch
HSE
Corex
References:
CR-GR-HSE-801 Management of HSE Events and Return on Experience
GM-GR-HSE-801 Guide for the Analysis of HSE Events
MAESTRO, 8th principle

## Slide 31
A video produced by the REX department explains the Company’s management of HSE events and REX process (3'50)
To be found in
the HSE Toolbox

## Slide 32: Findings: there is still room for improvement in the consideration of the recommendations of the REX
Recent findings (compilation of MAESTRO audits and some Branch surveys) show that the local management of the REX can still be improved:
  The affiliate or site does not have a COREX within the meaning of CR-GR-HSE-801.
  REX from the Branch is not processed because the local process is focused only on local incidents.
  The organization is disseminating the REX in the organization without giving meaning to the interest of taking it into account, especially to the frontline people.
  Recommendations are not transformed into action plans and their implementation is not monitored regularly.
  The REX are not used daily to learn about the past, to share about the mains causes of the accidents or to prepare the risk analysis, shutdowns, projects, trainings, etc.
Notes: Implementing REX: implementing sustainable, targeted measures requires sharing and explaining with the field the positive impact that REX should have on our operations.

## Slide 33: A successful REX process means:
Reporting the HSE incident
Gathering information
about the HSE incident
Analysis
of the HSE
incident
Sharing
information
with the
right people
Implemen-tation and follow-up of recommend-dations
We all have a role to play in contributing to the REX performance
Working in a multidisciplinary team. Appoint people in charge of actions. Explain in the field why this REX is important and what its implementation will bring. Ensure the implementation of actions.
... systematically
…as quickly as possible
…by integrating HOF*
... up to the field
... with regular review of actions
* Human and Organizational Factors. See GM-GR-HSE-350

## Slide 34: The main role of the local HSE Corex
Interbranch
Company HSE
Corex
Systematic reporting of HSE events and good practices
Serious accident, HiPo, ...
Another LBU accident
Good practice
Pluridisciplinary analysis
Implementation of recommendations: Explanation to the appropriate people, actions plan and follow-up
Implementation = saying “Why” this REX is important rather than saying “How”
Local
HSE
Corex
Actions plan
Local best practices
Appoint a REX coordinator and convene a Corex on a regular basis.
Organize the Corex with a multidisciplinary team and a decision-maker.
Integrate REX from other sites and Branches.
Appoint people in charge of actions and monitor their implementation. Explain in the field why this REX is so important and what its implementation will bring. Use the REX for risk analyses, works, projects, training, etc..
Branch
HSE
Corex
Analysis and selection
Selection
Recommandations
START
END
Notes: The local Corex can be organized at the level of a site, a facility (FPSO, depot, refinery), an affiliate or an activity (service station network, gas plant network, etc.).

## Slide 35: Read more...
Reference documents
  GM-GR-HSE-351 Approaches for an Integrated Safety Culture.
  CR-GR-HSE-801 Management of HSE Events and Return on Experience.
  GM-GR-HSE-801 Guide for the Analysis of HSE Events.
  MAESTRO, 8th Principle.
Training (available on Lizzy)
  HOF for an Integrated Safety Culture.
  Technological risks awareness.
  More specific training in technological risks: management of technological risks, asset integrity, safety in design and engineering upstream & downstream, Awareness of safety engineering for MS industrial projects. Event Analysis and REX Training.
  And trainings on category HSE: HSE MANAGEMENT / REPORTING, INCIDENT ANALYSIS AND REX / COMPANY CATALOG

## Slide 36: Organizing the WDfS
05.

## Slide 37: The WDfS 2024 poster
This poster is available in 9 languages (French, English, German, Dutch, Spanish, Italian, Portuguese, Chinese and Arabic) and in multiple formats: jpeg, pdf HD et BD, PPT…
Available in
the HSE Toolbox

## Slide 38: Find the communication media of WDfS 2024
Form to collect
feedback from
participants
HSE Toolbox
Manager Kit
(FR and EN) with the workshop guide included
POSTER
Major accident media
(PPT, videos),
TotalEnergies HSE Toolbox | Toolbox HSE
Note: the HSE Toolbox is an external site, accessible to all, without any password

## Slide 39: Facilitate the WDfS 2024 in your affiliate / site
WDfS is a time to celebrate Safety at any Company's headquarters, affiliates and sites.
It brings together employees from TotalEnergies and partner companies.
You can choose different activities, depending on your situation / activity:
  A workshop (recommended, see part 06.), talk or presentation with employees and partner companies.
  Discussion on the major risks management, compliance with current rules, elements of progress (safety green light, joint safety tours, life saving checks …).
  Presentation / demonstration of internal and external REX implementations or good practices (Safety+ ...), with partner companies.
  Safety Awards ceremony.
  Any other activity that meets your expectations, rituals of your entity.

## Slide 40: Engaging partner companies
Safety is for all, whether TotalEnergies employees or partner companies' ones. It is important to involve the partner companies of your affiliate/site in the WDfS.
TotalEnergies and partner companies: everyone’s involved!
Ask your partner companies to participate in your workshops, or co-animate them, or create their own workshop to share experiences together

## Slide 41: How to organize the workshop ?
This guide is designed to help you facilitate the workshop locally or remotely
06.

## Slide 42: Objectives
  During the World Day for Safety 2024, we invite you to organize exchange workshops with TotalEnergies and partner companies’ employees on the theme “Major Accidents and REX”.

## Slide 43: How to prepare the workshop?
  Terms?
    Approximately 1 hour; To be book. Invite employees in advance (groups of 5 to 20 people maximum). In buildings and on the field (control rooms, maintenance workshop, company village, etc.).
  Who is involved?
    Employees of TotalEnergies and partner companies and also the visitors present the D-day.
  Who is leading the workshop?
    Member of a Codir.
    Local manager with his/her counterpart from a partner company (co-facilitation).
    Manager of a partner company.
  What's next?
    A sharing form for all the participants of the activities from TotalEnergies and contractors.
    A web platform to collect photos, videos, appreciation.
Standard invitation message
    "On the occasion of WDfS 2024, we invite you to participate in a workshop on the theme of this year: Major Accidents and REX. For an hour, using the example of known major accidents, we will discuss about the importance of remembering major accidents, how the REX has improved our Safety and the importance of applying the REX within our affiliate or site. Don't forget to sign up. See you the 22nd of April.”

## Slide 44: Media available (in addition to the Manager Kit)
WDfS Poster.
Kakemonos.
Company videos.
  Corporate message from Pol Hoorelbeke, VP Major Risks (posted online on April 22).
  Videos of testimonies about 3 different major accidents (available a few days before the WDfS).
Manager Kit slides and other media (videos, PPT) summarizing the 9 major accidents selected by the Branches.
Links to feedback surveys for the participants and web platform for a local organizer.
T-Shirt template.
Progressively available in the HSE Toolbox

## Slide 45: How to facilitate the workshop?
  Your role is to lead a moment where everyone will have the opportunity to understand and express themselves about major accidents and REX by facilitating exchanges, adopting a neutral posture, without value judgement.
Follow these animation tips:
  Listen attentively, make sure that everyone can participate and express themselves, without fear of the gaze of others.
  The exchange workshop should allow everyone to collect information and express their point of view.
  Facilitate exchanges and encourage people to speak out.
Your role as a facilitator
    Setting the wrong tone
    Prevent the group from coming to its own conclusions
    Focus on problems rather than solutions
    Leading the discussion too quickly
    Making Too Many Suggestions
    Losing track
6 traps to avoid

## Slide 46: How to run the workshop?
Introduce yourself, thank the participants, present the topic of WDfS and the objectives of the workshop:
    Raise awareness of major accidents and what they have changed for the Company.
    Discuss knowledge of these accidents and awareness of the most important risks in the affiliate/site.
    Know the importance of return of experience (REX).
    Understand how to properly manage the REX locally to ensure its implementation (explaining the REX to the appropriate people, implementing recommendations and following up the actions).
    Looking for ideas to develop knowledge of major accidents, risk awareness, implementation of REX locally.
5 min.
1

## Slide 47: How to run the workshop?
Involve the group
A. Ask open-ended questions to workshop participants about their knowledge of historical major accidents:
  When you think of a “major accident of the energy industry or the company”, what event do you think of? Can you explain it to others?
  What do you think this event has changed in terms of safety for the industry? For the Company?
  Could you give an example of a corrective action or mitigation measure that has been put in place since then?
2
40 min.

## Slide 48: How to run the workshop?
B. Review the part 02. of the Manager Kit “Knowing Major Accidents and what they have changed for the Company”
  And choose one or two emblematic accidents from the 9 selected by the Branches to share with your team the facts, causes, consequences and what it has changed for the Industry or the Company.
Exchange and share your knowledge, experiences, perceptions on significant risks:
  Only humans have memory! How can we collectively remember these major historic accidents?
  What are the most important risks of our affiliate/location/industry?
  How to develop awareness of these most important risks?
    E.g. simulating dangerous phenomena? Sharing risk analyses? Getting witnesses to talk about major accidents?, …
+ Toolbox HSE : additional documents to explain the accident(s) chosen
Note: these 9 accidents were particularly selected by the Branches because of the importance of their consequences and the impact of their return of experience for the Company. Depending on your situation, you can select other important accidents from your affiliate/site, an Hipo,... and discuss the consequences of this accident and how it has been considered to improve our Safety.
2
40 min.
48
2005 - Buncefield (MS)
2010 - Deepwater Horizon (EP)
1988 – Piper Alpha (EP)
1999 – Erika (TS)
2001 – Teeside Enron (GRP)
2013 Ooltgensplaat Fire (GRP)
2017 – Qapco (RC)
2018 – Mostorod (MS)
2019 – Normandie (RC)

## Slide 49: How to run the workshop?
C. Review the parts of the Manager Kit on the REX:
  Part 03 “Return of experience, how does it work and what are the main benefits?”
  Part 04 How to well manage the REX in your affiliate / site?
  And remember:
    The general principle of return of experience
    The 4 benefits of REX:
      Avoiding further accidents.
      Improving our standards and making it easier to assimilate the rules.
      Remembering accidents and lessons learned to use them daily.
      Advancing the best practices.
    The performance elements of the REX
    How to well manage the REX locally ?
      including the Company's Rex Process video 3’50.
2
40 min.

## Slide 50: How to run the workshop?
D. Ask questions about the REX:
  Have you understood the principle and the value of return of experience?
  Do you report accidents, near-misses and anomalies systematically?
  Are you familiar with the REX relative to your unit, department, network, or activity?
  Are you aware of the REX coming from your Branch, from other Branches, from other compagnies?
  Before a work (or a risk analysis or a training), do you check the REX in databases to improve your knowledge of the situation ?
  Do you know how to search for the Company's REX on the databases?
  Have you any ideas to advance the implementation (sharing, actions plans and follow-up) of REX in your affiliate/site, in the Company? And how to share it with our partner companies?
2
40 min.

## Slide 51: How to run the workshop?
  Summarize the different ideas…
  Pick up and gather the strong ideas put forward by the participants.
Workshop feedback: encourage each participant to fill in the form, with, among other questions, a request for feedback on the following questions:
  Do you have any ideas for everyone to remember the major historical accidents?
  An ideas to develop awareness of the most important risks in your affiliate / site / branch / Company?
  Have you any ideas to advance the implementation (sharing, actions plans and follow-up) of REX in your affiliate/site? At the Company level?
  Do you have any ideas or best practices to promote the sharing of REX with partner companies?
Reminder:
Implementation of REX
Explanation to the appropriate people, actions plan and follow-up
saying “Why” this REX is important rather than “How”
4
3
5 min.
10 min.

## Slide 52: And, just like every year...
A specific web platform will allow you to share photos and videos of your event. The link will be communicated in April in various media (pushmail, HSE Toolbox, etc.)

## Slide 53: Enjoy your World Day for Safety 2024!