## Slide 1
Golden Rule 9 Excavation Work
The new Golden Rules
My Commitment, our Safety
Rev.0 – December 2022

## Slide 2
01. The essentials

## Slide 3: Poster & pictogram
The Golden Rule 9 pictogram "Excavation Work" shows the arm of an excavator extracting soil. The extracted material is also shown at the edge of the excavation.

## Slide 4: Some definitions
Air pick
Vacuum excavator with a soft tip
Pickaxe
Jackhammer
Trencher
Truck-mounted drilling rigs
Any trench, cavity, cut, or hole in the ground involving the extraction of soil or rock, including geotechnical drilling and pile driving.
EXCAVATION
A long, narrow excavation in the ground whose depth is equal to or greater than its width measured at the bottom of the excavation.
TRENCH
Soft or “non-aggressive” excavation techniques
Hand shovel
“Aggressive” excavation techniques
Mechanical excavator (digger, mini digger…)
Vacuum excavator with a rigid tip

## Slide 5: The essence of Golden Rule 9
    Mention of the "Excavation certificat":
    The identification of underground structures or networks is formalized by an excavation certificate prior to the permit to work.
    Mention of the "Secured access":
    For excavations >1.3m deep, means of safe access* are provided and inspected daily before the personnel enter the excavation.
    This depth of 1.3m** may vary according to local regulations.
What changes from the 2017 version of the Golden Rules:
Excavation Works are covered in CR-GR-HSE-425 "HSE Requirements for Excavation Worksʺ ***.
Stairs with handrail, ladder, ramp, etc.
** Requirements 3.3.1 et 3.3.3 of CR-GR-HSE-419, Labour Law (art. R4534-24), American Regulations (OSHA 2226-10R 2015)
*** Company Rules (CR) are limited to internal use.
    The excavation certificat does not autorise to start the works.

## Slide 6: Excavation Work incidents
Objects falling into the excavation
Risk of dangerous atmosphere
Cave-in / wall collapse on personnel in the trench
Burns or electrocution owing to contact or an electric arc with overhead electrical lines
Risks related to hitting an active underground network
Machinery/equipment falling or toppling over
Risks related to the movement of excavating machines
ACCIDENTS IN THE COMPANY WHERE A REQUIREMENT OF GOLDEN RULE 9 HAS BEEN BREACHED
* 2012-2021 ** 2017-2021
Fatalitiy*
0
Lost time accident**
1
HIPO (High Potential)**
17
MAIN RISKS OF EXCAVATION WORK
Personnel falling

## Slide 7
02. REX

## Slide 8: Illustration of requirements
The descriptions of the circumstances and consequences have been simplified for a better understanding.
A link to each REX is available for more information.
REQUIREMENT | EVENT | SLIDE
1. I have a work permit and an excavation certificate. | ACCIDENT IN A DEPOT DURING EXCAVATION WORK | N°9
2. I confirm that the excavation area is clearly marked off. | BURNS TO THE LEG IN A TRENCH FILLED WITH HOT WATER | N°10
3. I stay alert to the location of underground structures and networks. | GAS PIPE PERFORATED DURING DEMOLITION WORK | N°11
4. I position machinery at least one meter away from the excavation area. | SHOCK TO THE HEAD FOLLOWING THE TIPPING OF AN EXCAVATOR | N°12
4. I position extracted material at least one meter away from the excavation area. | LEG CONTUSION DUE TO FALLING ROCKS | N°13
5. I only enter an excavation deeper than 1.3m if the access is secured. | ENTERING INTO AN EXCAVATION >1.3 M | N°14

## Slide 9: REX
Victim
1. I have a work permit and an excavation certificate.
> ACCIDENT IN A DEPOT DURING EXCAVATION WORK
CIRCUMSTANCES – FACTS
  Excavation work was carried out by an external company.
  A few days later, the foreman of this external company asked his worker to remove soil and stones in a 2 m deep trench.
  A concrete slab (500 kg) broke away from the edge of the trench and buried the worker.
CONSEQUENCES
Fractures to the shoulder, rib and right leg.
CAUSES
  Lack of securing of trench walls > 1.3 m deep. The trench walls collapsed, causing the slab to collapse.
  No work permit was obtained for this unplanned manual excavation.
  No risk assessment or safety green light was carried out before the work began.
I ensure that I have the excavation certificate and work permit associated with my excavation work before I start any excavation work.
I ensure that the sides of the excavation are fitted to prevent cave-ins if a worker is to access.
LESSONS TO BE LEARNED
Click here to access the REX

## Slide 10: REX
2. I confirm that the excavation area is clearly marked off.
> BURNS TO THE LEG IN A TRENCH FILLED WITH HOT WATER*
CIRCUMSTANCES – FACTS
  During a tour, a worker stepped into a 30 cm deep pit behind him.
  This was filled with stagnant water heated by a buried pipe (drain of a boiler tank).
CONSEQUENCES
Burns on the lower left leg and several weeks off work.
CAUSES
  Lack of protection of the excavation at the time of the event.
I make sure that the excavation area is marked off. If there is a risk of a person or machine falling into the excavation, a rigid barrier must be installed:
Pit filled with hot water
* Event prior to 2021
Rigid physical barrier
Concrete guardrail
For people
For engins
As a reminder, the excavation area is the maximum extension of the area where the excavation is planned.
LESSONS TO BE LEARNED
Click here to access the REX

## Slide 11: REX
3. I stay alert to the location of underground structures and networks.
> GAS PIPE PERFORATED DURING DEMOLITION WORK
CIRCUMSTANCES – FACTS
  During demolition work on a car wash, a town gas pipe 65 cm below the ground was punctured by the tip of a rock breaker.
  This incident caused a release of pressurised gas.
CONSEQUENCES
No actual injury, but potential fire/explosion (HIPO).
CAUSES
  Unreliable existing plans.
  Lack of verification of the actual location of networks identified in existing plans.
I ensure that the actual location of buried structures or networks is accurately determined, in particular :
  by using existing plans
  by consulting the operators of third-party structures or networks
  by checking the location of the networks identified by additional investigations
If necessary, I report any discrepancies identified.
LESSONS TO BE LEARNED
Click here to access the REX
Service station building
Washing gutter
Actual location of the gas pipe
Boundary of the concession
m
Assumed location of the gas pipe

## Slide 12: REX
LESSONS TO BE LEARNED
4. I position machinery at least one meter away from the excavation area.
> SHOCK TO THE HEAD FOLLOWING THE TIPPING OF AN EXCAVATOR
CIRCUMSTANCES – FACTS
  A civil engineering company had to carry out two tasks: loading compost into big bags and placing gravel at the bottom of the excavation.
  During the preparation of the bottom of the excavation, the excavator, which was mounted on the compost heap, tipped over.
  In its movement, it hit a ladder leading to the bottom of the excavation, which itself tipped over and hit a worker present in the excavation.
CONSEQUENCES
Several potential fatalities (HIPO).
Concussion to the head without wound.
CAUSES
  Incorrect positioning of the excavator which led to its tipping over.
  Worker at the bottom of the excavation while backfilling was in progress.
  Access ladder not fixed.
I ensure that the equipment is positioned more than 1m from the excavation to prevent it from tipping over into it.
Click here to access the REX

## Slide 13: REX
LESSONS TO BE LEARNED
4. I position extracted material at least one meter away from the excavation area.
> LEG CONTUSION DUE TO FALLING ROCKS
CIRCUMSTANCES – FACTS
  While a worker was removing stones from a trench to lay cables, a previously excavated rock fell back into the trench, injuring the worker.
CONSEQUENCES
Leg contusion and 11 days off work.
CAUSES
  Decrease in the distance between the excavated material storage area and the trench, due to an increase in the number of trenches for cable laying.
  Lack of identification of the additional risk generated by additional excavations.
  A jackhammer working nearby could have induced vibrations.
I ensure that excavated material is positioned more than 1m from the excavation to prevent it from falling back into it.
Example of a rock
Click here to access the REX

## Slide 14: GOOD PRACTICE
5. I only enter an excavation deeper than 1.3m if the access is secured.
> GOOD PRACTICE FOR ENTERING INTO AN EXCAVATION >1.3 M
  Safe access to an excavation area is essential to prevent the risk of falls and to allow easy evacuation in an emergency.
  Use stairs, earth ramps or ladders.
  Create a walkable access on each side of the excavation and equip stairs or ramps with handrails.
  In the case of trenches, personnel inside the trench should not walk more than 8m to find a safe means of exit.
  If ladders are used, they should be installed between 65° and 75°, stable (fixed at the base or at the top) and extend at least one metre above the top of the trench.
  When accessing a deep excavation with a long ladder, it is advisable to fit the operator with a fall arrest system attached to an anchor point fixed to the shoring.
  Manage water run-off to maintain access and allow descent into the excavation in all weather conditions.

## Slide 15
03. Further information

## Slide 16: Our tools and documents
CR-GR-HSE-419 – HSE Requirements for excavation works: HSE Company Rules
Life Saving Checks – Excavation Works: Life saving checks
E-learning on excavation works: https://lizzy.totalenergies.com/
Toolbox HSE – new Golden Rules:
    General material: TotalEnergies Golden Rules – General material
    Roll-out material: TotalEnergies Golden Rules – Roll-out material
REX database: Group_HSE_REX DataBase
Safety+ (good practices per Golden Rule): https://safetyplus.totalenergies.com/en
    Some good practices:
          https://safetyplus.totalenergies.com/en/contribution/tq80bd
          https://safetyplus.totalenergies.com/en/contribution/ec83nz
          https://safetyplus.totalenergies.com/en/contribution/6u5m2x

## Slide 17: Lexicon
Hazard: An intrinsic property of a product, equipment, process, situation or action that can result in harm to people, the environment and/or assets.
Risk: The combination of the probability of occurrence of a hazardous event and the severity of the impact that may result from exposure to the hazard.
HSE events:
  Incident: Any sudden and undesirable HSE event on a given date, that causes injury or illness, damage to property or facilities, loss of production, environmental damage or damage to the Company's image.
  Near miss: Any sudden and undesirable HSE event on a given date which, in slightly different circumstances, could have had the same consequences as an incident. A near miss does not have an actual severity level but has a potential severity level.
  Anomaly: Any abnormal situation or behaviour, including deviations from a standard, specification, procedure or rule.
HIPO (High Potential) [slide 6]: Incident or near miss with an actual severity level ≤ 3* and a potential severity level ≥ 4** in one or more areas of the Company’s evaluation matrix of the actual and potential severity level of HSE events.
REX HSE: Document for sharing information on an internal or external HSE event, based on a detailed analysis and making recommendations.
* For example, physical consequences with an actual severity level = 3 correspond to a lost time accident.
** For example, physical consequences with a potential severity level of 4 correspond to a fatality.
Notes: Définitions « risques » et « danger » (GM-GR-HSE-300 « Evaluation des risques professionnels au poste de travail »)
Définitions HIPO, Incident, presqu’accident, anomalie (CR-GR-HSE-100 « Reporting HSE »)