## Slide 1: Major Technological Risks and Critical Barriers
Company Rule CR-GR-HSE-403
Notes: Afin de respecter la dénomination de la Marque, merci de veiller à la bonne orthographe de TotalEnergies.
TotalEnergies s’écrit en un seul mot, sans espace, avec un « s » à la fin, avec le T et le E en majuscules, les autres lettres en minuscules, et pas d’accent sur le E majuscule.
Elle s’écrit bien TotalEnergies et non :
Total Energies (avec un espace)
totalenergies
total energies
Totalenergies
Total energies
totalEnergies
total Energies
TOTALENERGIES
TOTAL ENERGIES

## Slide 2: CR-GR-HSE-403
Purpose
This rule defines HSE requirements for the management of major technological risks and safety and environment critical barriers.
This rule was approved by the HSE Committee on September 23, 2022
Replaces (partially or totally)
1 Directive DIR-GR-HSE-018 Technical Integrity Management
4 Rules in Branches CR-EP-HSE-047 Technical Integrity Management
CR-RC-HSE-104 Technical Integrity Management
CR-RC-HSE-145 Critical Measures for Safety and Environment
CR-MS-HSEQ-341 Management of Technical Integrity of Facilities and of Downgraded Situations

## Slide 3: Structure : 7 themes, 16 requirements
  Management of Critical Barriers
  Major Threats Identification
  Major Risks Action Plan
  Organisation
  Documentation review
  Performance review
2
3
4
5
6
7
1. Major Technological Risks
2. Identification of Critical Barriers and their components 3. Performance Standard 4. Test, Inspection and Preventive Maintenance Program 5. Backlog management when executing the Test, Inspection and Preventive Maintenance Program 6. Managing Deviations from Performance Standards and the Unavailability of Critical Equipment 7. Audit of the Test, Inspection and Preventive Maintenance Program 8. Critical Human Component of a Critical Barrier
9. Identifying and Assessing Major Threats
10. Major Technological Risks Action Plan
11. Process Safety 12. Process for Managing Critical Barriers and the Major Technological Risks Action Plan 13. Guardian of Critical Equipment 14. Competencies and Training
15. Periodic Documentation Review
16. Steering Committee
  Major Risks Identification
1
Level of change low medium large

## Slide 4: Applicability
« This rule is applicable by all Company entities and affiliates that operate major technological risk installations as presented below, in accordance with their respective decision-making rules:
All installations using substances that are ‘named’ or ‘falling under’ the hazard categories, and which are at, or above the lower-tier quantity requirements (including after the accumulation rules), specified in European Directive 2012/18/EU known as the ‘SEVESO’ Directive. This is regardless of whether they are subject to the regulations of this Directive or not;
All installations defined in European Directive 2013/30/EU concerning the safety of offshore oil and gas operations, and regardless of whether they are subject to the regulations of this Directive;
Wells and associated installations, and pipelines.
Date of application: ▪ New Projects: from the publication date of this rule;
▪ Existing Installations: 12 months after the publication date of this rule.

## Slide 5: Review of requirements
Requirement 3.1.1: Major Technological Risks
Major Technological Risks are identified on each site.
Requirement 3.2.1: Identification of Critical Barriers and their Components
The critical barriers of an installation, along with the critical equipment and critical human components, are identified using one of the methods described in GS-GR-HSE-311.
A register of critical barriers specific to each site and/or operating unit is available and kept up to date.
Requirement 3.2.2: Performance standard
The performance standard of a critical equipment is defined in the design stage as per GS-GR-HSE-311 and updated throughout the life of the installation to factor in aging, changes in organization and equipment, and possible failure modes.

## Slide 6
Requirement 3.2.3: Test, Inspection and Preventive Maintenance Program
A program of testing, inspection and preventive maintenance is implemented and monitored throughout the life of the installation.
The performance of each critical equipment is measured, recorded and regularly analyzed.
The status of each critical equipment is available in the critical equipment management system (Computerized Maintenance and Inspection Management System or equivalent).
Requirement 3.2.4: Backlog management when executing the Test, Inspection and Preventive Maintenance Program
Any delays in the execution of the critical equipment test, inspection and preventive maintenance program are tracked on a monthly basis, subject to analysis, and validated at the appropriate level of the entity or affiliate.
Review of requirements

## Slide 7: Review of requirements
Requirement 3.2.5: Managing deviations from Performance Standards and the unavailability of critical equipment
Any deviations of critical equipment from their performance standard, as well as cases of unavailability, are identified and recorded.
The impact on critical barriers and associated risks are assessed.
An action plan including temporary compensatory measures and corrective measures is implemented and monitored at the appropriate level of the entity or affiliate.
Requirement 3.2.6: Audit of the Test, Inspection and Preventive Maintenance Program
The planning, execution, monitoring and relevance of the critical equipment test, inspection and preventive maintenance program are regularly audited.
The entity in charge of the audit is independent from the department in charge of test, inspection and preventive maintenance activities.

## Slide 8: Review of requirements
Requirement 3.2.7: Critical Human Component of a Critical Barrier
A human action identified as a critical human component of a critical barrier is subject to a procedure or an authorization.
Knowledge and application of those procedures are regularly tested, and conformity of authorization is regularly audited.
Requirement 3.3.1: Identifying and Assessing Major Threats
Major Threats, characterized by the failure, inadequacy or absence of a critical barrier or set of barriers are identified and formally defined.
Requirement 3.4.1: Major Technological Risks Action Plan
A major technological risks action plan is available on each site or operating unit and is communicated to personnel. It is associated to :
Major first priority or non-ALARP scenarios identified by technological risks studies ;
Major Threats.
and specifies their level of risk.
This action plan is implemented to return as quickly as possible to the level of risk validated in the initial design phase of the installation, or, if this risk has not been assessed in the initial design phase, to bring it down to an acceptable level or tolerable if ALARP.
Each major technological risks action plan is approved by the manager of the entity or affiliate.

## Slide 9: Review of requirements
Requirement 3.5.1: Process Safety
Evaluation of major technological risks and identification of associated of critical barriers are conducted by a person competent in process safety.
Requirement 3.5.2: Process for managing Critical Barriers and the Major Technological Risks Action Plan
The HSE manager is responsible for Major Technological Risks and Critical Barriers management.
A process is defined and implemented to manage critical barriers and the major technological risks action plan.
This process is documented. It meets all the requirements of this rule and defines the roles and responsibilities of the key players in the process.
A Leader is appointed and is in charge of this process; it is the HSE manager or a person reporting to him.
He steers the process, in order to propose to the management committee a global view of the associated risks. He meets periodically, as needed, with operational managers to share the progress of the major technological risks action plan.

## Slide 10: Review of requirements
Requirement 3.5.3: Guardian of Critical Equipment
A guardian is formally identified for each critical equipment.
Guardians ensure that the performance standard associated with each critical equipment is respected, by checking that :
  The test, inspection and preventive maintenance program is carried out ;
  Any deviations are addressed ;
  The test, inspection and preventive maintenance program and the list of critical equipment are updated.
Requirement 3.5.4: Competencies and Training
The personnel involved in implementing the critical barrier management process and major technological risks action plan are competent.
In particular the leader of the critical barrier management process and the major technological risks action plan has in-depth knowledge of the production installations, and if possible, managerial experience in operations.

## Slide 11: Review of requirements
Requirement 3.6.1: periodic documentation review
The following documents are reviewed whenever the technological risk study is updated :
  The critical barrier register ;
  The performance standards associated with the critical equipment ;
  The major technological risks action plan.
Requirement 3.7.2: Steering Committee
A steering Committee meets at least once a year to review the process for managing the performance of the critical barriers and the major technological risks action plan.
A summary of this review is communicated to the management team of the relevant branch. The summary specifies at least the status of the major threats and the non-ALARP major risks (identified in the technological risks studies) as well as the associated action plans.
The Key Performance Indicators (KPIs) established at company level, are monitored by each entity or affiliate. They are complemented by other performance indicators specific to each branch, and where necessary, by performance indicators specific to the entity or affiliate.