## Slide 1: Safety of Maritime and Inland Waterway Terminals HSE GROUP RULE (CR-GR-HSE-422)
SUMMARY
This rule defines the minimum HSE requirements for the management of risks associated with the loading, unloading and bunkering of vessels and barges with dangerous liquid bulk cargoes at maritime or inland waterway terminals

## Slide 2
Context:
    Activity in our Oil & Gas terminals
    Maritime : 49 terminals - 70 Mt/y – 1800 calls/y
    Inland Waterways : 27 terminals - 13 Mt/y – 5500 calls/y
Scope: all entities of the operated domain
Defines 15 requirements, grouped into 3 themes:
    Identification of Risks
    Risk Control Measures of fire / Explosion, mooring failure, loss of containment, drowning
    Training, Emergency Response Plan, HSE Event Reporting, Self Assessment
Remplacing branch document :
    CR MS HSE 640 Marine and Inland Waterway Terminal Safety
    CR RC HSE 045 Marine and Inland Waterway Terminal Safety
Modificating branch document :
    CR EP LSO 200 Management of Marine Operations
    CR MS LOG 003 Receipt by barges and vessels
Date of publication in REFLEX: 30/09/2020
Effective date: 31/12/2020
CR-GR-HSE-422

## Slide 3
REQUIREMENTS
Requirement 3.1.1 : HSE Risk Identification
Operations related to the loading, unloading and bunkering of vessels and barges with dangerous liquid bulk cargoes in terminals undergo an HSE risk identification exercise that factors in at least: The nature of the substances transferred; The metocean conditions; The phases of activities listed in Appendix 1; The potential interfaces with co-activities, including nearby maritime or inland waterways traffic.
No significant change
Already required in DIRSEC-16
(§2 – Risk Analysis)
The risks are identified by specific studies carried out during the design stage, supplemented by hazard identification studies (HAZID) and operational hazard identification studies (HAZOP), and updated regularly during the life cycle of the installation.
At the end of these studies:
The proposed risk controls give priority to the implementation of prevention means, mitigation measures and to the rapid detection of incidents, in order to activate emergency plans as quickly as possible when necessary;
The technological risks identified are managed in compliance with CR-GR-HSE-301.
RISK MANAGEMENT

## Slide 4
REQUIREMENTS
Phases of Activity to be considered in Risk Identification.
Nautical access to the terminal (where applicable – usually the responsibility of the port authority);
Berthing and/or mooring, including double banking with another vessel or barge;
Access routes for personnel on board;
Transfer operations, including during transition periods (at the beginning or end of (un)loading, transhipment and/or bunkering operations);
Connection and disconnection, purging/draining of cargo transfer and/or vapour return equipment;
Gauging and/or sampling;
Recovery of vapours from the vessel or barge unit to the terminal (where applicable)
APPENDIX 1

## Slide 5
REQUIREMENTS
Requirement 3.2.1 : Hazardous Area Classification
Areas of the terminal facilities where potentially explosive atmospheres may occur are classified according to local regulations, or failing this, according to the requirements of the European ATEX Directive no.1999/92/EC or of the international standard IEC 60079-10-1.
No significant change
In particular:
      Diagrams (plan and elevation views) show the hazardous areas;
      Warning signs are placed at the entrances to areas where explosive atmospheres can form;
      The electrical, electronic, telephone, and radio equipment (VHF/UHF) used or likely to be used in these areas are certified;
      The hand tools used in these areas are designed and adapted to reduce the risk of sparks, particularly when connecting and disconnecting hoses or arms.
MEASURES TO CONTROL FIRE AND EXPLOSION RISKS

## Slide 6
REQUIREMENTS
NEW
Requirement 3.2.2 : Electrical Isolation of Connection Elements Between the vessel or Barge and the Terminal
In areas with potentially explosive atmospheres, electrical insulation is provided on all the connecting elements between the vessel or barge and the terminal, including arms, hoses, gangways and access walkways, fendering systems and mooring lines in order to avoid any risk of electric arcs. The effectiveness of this insulation is checked on a regular basis.
New requirement for all branches based on a specific study and recommended by O&G industry
Electrical insolation of the arms => insulation flange.
Electrical insolation of hoses => insulation flange or an electrically discontinuous hose string.
Bonding cables are not an effective means of dissipating potential differences between the vessel or barge and the terminal. They are used only when required by local regulations.
Specific study : A justification into the use of insulating flanges (and electrically discontinuous hoses) at the ship/shore or shoip/ship interface (SIGTTO)
MEASURES TO CONTROL FIRE AND EXPLOSION RISKS

## Slide 7
REQUIREMENTS
Requirement 3.2.3 : Protection Against the Risks Related to Static Electricity During the Loading Phases of Non-inerted Tanks
The initial and maximum transfer flowrates of products that accumulate static electricity in non-inerted tanks of a vessel or barge are determined, and this information is exchanged before the transfer between the vessel or barge and the terminal.
No significant change
Applied in all terminals
linear transfer velocity is limited to a maximum of 1 m/s at the individual tank inlets during the initial phase of loading
then limited to maximum 7 m/s.
Not applicable to the loading of liquefied gas on vessels or barges gassed-up tanks.
GNL
GPL
MEASURES TO CONTROL FIRE AND EXPLOSION RISKS

## Slide 8
REQUIREMENTS
Requirement 3.3.1 : Mooring of the Vessel or Barge
Taking into account the metocean conditions and physical phenomena associated with maritime or inland waterway traffic passing nearby, the terminal ensures that for each berth and for different sizes of moored vessel or barge the following is defined: Minimum under-keel clearance (UKC); Minimum mooring requirements and performance criteria; Additional measures to control the risk of mooring failure and the associated potential consequences, where appropriate.
No significant change
Applied in all terminals
Access to maritime and inland waterway expertise already in place
(§5.3 of the DIRSEC 16)
In order to do so:
    Metocean limits are defined;
    A specific study is carried out with the help of the port authority or other maritime or river expertise for each berth.
Additional measures to control the risk of mooring failure and the associated potential consequences may be, for example:
The reinforcement of the mooring;
The assistance of tug(s);
Stopping transfer operations;
Disconnecting hoses or loading/unloading arms;
A safety distance or navigational restriction zone for ships or barges passing nearby;
breakaway coupling for the hoses or a PERC (Powered Emergency Release Coupling) for the loading/unloading arms;
the installation of a non-return valve when the transfer line is dedicated to unloading.
MEASURES TO CONTROL THE RISK OF MOORING FAILURE

## Slide 9
REQUIREMENTS
Requirement 3.4.1 : Loss of Containment Detection
Depending on the nature of the products, appropriate means are implemented to detect any loss of containment of flammable or toxic liquid, gas and other vapours during transfer operations. In particular: Pipelines running over or close to bodies of water, as well as the arms and hoses, are visually inspected at an adequate frequency; The deviation of the quantities transferred between the terminal and the vessel or barge is checked at least once per hour.
No change
Already required in DIRSEC-16
(§5.1 - Supervision)
Applied in all terminals
The pipelines, arms and hoses undergo preventive maintenance at a justified frequency. The follow-up of this maintenance is documented.
When cameras and/or other means of detection are used, they are:
Sufficient in number;
Regularly checked and controlled;
Started up upon arrival and until departure of the vessel or barge.
The installation of cargo containment is recommended
MEASURES TO CONTROL THE RISK OF LOSS OF CONTAINMENT

## Slide 10
REQUIREMENTS
NEW
Requirement 3.4.2 : Hose integrity
Taking into account the regulatory obligations and manufacturer’s recommendations, hoses used for transfer operations are: Appropriate for the nature of the products transferred; Identified; Visually inspected before each operation; Pressure-tested at a suitable frequency not exceeding: 1 year for onshore hoses; 3 years for offshore hoses; Withdrawn from service in the event of an anomaly or on a specified date. All hose integrity monitoring data (including those stored in the warehouse) are documented.
Applied in all terminals through inspection and maintenance plans
DIRSEC 16 § 3 – Integrity of the installations
New requirement for all branches on the frequency of pressure tests
Tests are conducted at a pressure equal to 1.5 times the Rated Working Pressure (RWP) of the hose and shall be supplemented, if necessary, by tensile tests at pressure and electrical continuity.
The specified disposal date can be imposed by regulations or defined according to the manufacturer’s instructions and/or the equipment criticality.
During the transfer operation, the bend radii are respected and, where necessary, the hoses are supported in order to avoid an overhang likely to affect the integrity of the manifolds.
The storage conditions of the hoses take into account the manufacturer’s recommendations
MEASURES TO CONTROL THE RISK OF LOSS OF CONTAINMENT

## Slide 11
REQUIREMENTS
Requirement 3.4.3 : Control of Isolating Valves
A check of the tightness and closing time of the transfer line isolating valves, generally located at the base of the arm (or the base of the hose) on the terminal side, is conducted at an adequate frequency, not exceeding 1 year. The follow-up of this inspection is documented.
No significant change
Applied in all terminals through inspection and maintenance plans
DIRSEC 16 § 3 – Integrity of the installations
The valve closure time is adapted to avoid any risk of surge pressure.
MEASURES TO CONTROL THE RISK OF LOSS OF CONTAINMENT

## Slide 12
REQUIREMENTS
Requirement 3.5.1 : Wearing a Lifejacket
In areas overhanging or bordering bodies of water: The wearing of life jackets is mandatory; Access is restricted to authorised personnel; Appropriate signage is visible nearby.
No significant change
Lifejackets comply with standard EN ISO 12402-3 or SOLAS standards and are maintained in accordance with the manufacturer’s recommendations.
In addition, these areas are illuminated in case of night-time operations, and are equipped with lifebuoys with a flashing light and lifeline, complying with the SOLAS standard
MEASURES TO CONTROL THE RISK OF DOWNING
Not applicable to permanently moored floating units (e.g. FSRU, FSU, FPU, FSO, FPSO) if the personnel are on decks equipped with permanent collective protection, such as guardrails.
Applied in all other terminals

## Slide 13
REQUIREMENTS
Requirement 3.6.1 : Approving the Vessel or Barge and Exchanging Information Before the Call
Before the call, the terminal: Makes sure that the vessel or barge is: - Physically compatible with the berth; - Approved by the Maritime and Inland Waterways Transport Vetting department in compliance with the applicable rule; Communicates the terminal’s information booklet to the vessel or barge within sufficient time.
No significant change
Already required in DIRSEC 16
(§6 – terminal’s acceptance of the ship/barge)
(§8 – Documentation)
Applied in all terminals
The criteria for evaluating the physical compatibility of the vessel or barge with the berth are detailed in Appendix 2.
The terminal’s information booklet contains:
Local regulations;
Nautical access constraints (if applicable);
Berthing and/or mooring constraints;
Physical and operational constraints at the berth;
General health, safety and security instructions and the action to be taken in the event of an incident or emergency.
It is recommended that the information booklet be written in English and/or in the working language of the terminal, if the vessel or barge operating personnel understand that language.
VESSEL OR BARGE APPROVAL AND INFORMATION EXCHANGE

## Slide 14
REQUIREMENTS
The criteria to assess the physical compatibility of a vessel or barge with a berth includes at minimum:
The water depth available allow the vessel or barge to remain afloat at all the tide levels expected during the call, taking into account a minimum under-keel clearance;
The mooring equipment and fendering systems (where applicable) are able to withstand the maximum specified loads without damaging the vessel (or barge) or the terminal’s equipment;
The fendering systems are positioned so that the vessel or barge can rest on the parallel body length and remain stable at all freeboards and all expected tide levels;
The safe working load (SWL) of the lifting equipment is sufficient to hoist the hoses on board the vessel (or barge);
The equipment used to board the vessel or barge complies with the tilt angle and weight (number of people) set by the manufacturer;
When connected, the (un)loading arms and hoses can move within a three-dimensional operating envelope, which factors in at least the following elements:
- The expected tide levels;
- The maximum and minimum freeboard of the vessel or barge;
- The acceptable differences in the horizontal alignment of manifolds;
- The distance of the manifolds from the side shell plating;
APPENDIX 2

## Slide 15
REQUIREMENTS
Requirement 3.6.2 : Information Exchange and Validation Before Starting the Transfer
Before starting the transfer, the terminal and the vessel or barge exchange the following information: The material safety data sheets (MSDS) of all products to be transferred; The list of co-activities planned during the transfer (onboard and/or in the terminal); The communication means to be used; The operating parameters (including at least the quantity, flowrate, pressure and temperature where applicable); Verification of the safety conditions; The measures to take in the event of an incident, an emergency situation or risk of lightning. The operating parameters and the safety conditions are verified and approved by the parties concerned and recorded in a dedicated document
No significant change
Already required in DIRSEC-16
(§4 – Communication with the ship or the barge)
Applied in all terminals
It is recommended:
To use the checklists recommended by industry
(ISGINTT => barges, ISGOTT or the Ship To Ship Transfer Guide => Vessels);
Periodically check the safety conditions every 4 hours
The co-activities planned may be the subject of a formal acceptance request by the vessel or barge and/or the terminal and/or the port authority.
VESSEL OR BARGE APPROVAL AND INFORMATION EXCHANGE

## Slide 16
REQUIREMENTS
NEW
Requirement 3.7.1 : Training of Personnel
The terminal manager, and any other person in charge of checking and approving safety conditions, have completed the online training course “Ship/Shore Safety Check-List” and obtained the certificate of achievement. Refresher courses are provided at regular intervals, not exceeding 5 years. Personnel involved in loading, unloading and bunkering operations are trained for the tasks under their responsibility. These training courses are recorded.
New requirement for all branches:
E-learning required for all terminal manager and all personel in charge of checking and approving ship/shore safety conditions.
Training course available on LIZZY
Duration : 45 mn
The training courses include for example:
Awareness of the risks related to the interface between the vessel or barge and the terminal (including the risks linked to broken mooring lines), the risks of the operations and products to be transferred, and the implementation of the applicable procedures;
What to do in the event of an incident or emergency situation (e.g. communication, evacuation, mustering point, use of safety and firefighting equipment and of accidental water surface pollution);
English courses for terminals involved with international traffic;
Verification of the physical compatibility between the vessel or barge and the terminal.
TRAINING

## Slide 17
REQUIREMENTS
Requirement 3.8.1 : Emergency Response Plan
The emergency response plan includes at least the following scenarios: Fire in the areas of the manifolds and product transfer equipment on board the vessel or barge or at the terminal; Spills affecting surface water with a severity of ≥ 3, according to the Group Evaluation Matrix of Actual or Potential severity levels of HSE events; Rescue of a person who has fallen into the water.
No significant change
Already required in DIRSEC-16
(§7 – Emergency Plans)
Applied in all terminals
EMERGENCY RESPONSE PLAN
Internal and external intervention and rescue means are regularly tested during exercises, the reports of which are recorded

## Slide 18
REQUIREMENTS
Requirement 3.9.1 : Communicating Brief Call Reports
If an HSE event involving a vessel or barge occurs during the call, the Brief Call Report is immediately communicated by the terminal to the Maritime and Inland Waterways Transport Vetting department.
No significant change
Already required in DIRSEC 16
(§6 – Brief Call Reports)
Applied in all terminals
The Brief Call Report enable the transmission of information on incidents, near-misses and anomalies involving a vessel or barge during the call.
It is available on the Group’s intranet.
DECLARATION OF HSE EVENTS

## Slide 19
REQUIREMENTS
NEW
Requirement 3.10.1 : HSE Self-assessment
The terminal’s HSE self-assessment protocol includes the chapters of the MTMSA (Marine Terminal Management and Self-Assessment) that address the following points: Port operations; Terminal layout; Vessel or barge / terminal interface; Transfer operations; Operations at buoy moorings (where applicable); Terminals impacted by frost, ice or severe sub-zero air temperatures (where applicable).
New requirement for all branches
(See next slide)
CR-GR-HSE-902 describes the HSE self-assessment requirements.
HSE SELF-ASSESSMENT

## Slide 20
REQUIREMENTS
 |  |  | Questions
Common part | Element 1 | MANAGEMENT, LEADERSHIP AND ACCOUNTABILITY | 
 |  | MANAGEMENT, LEADERSHIP AND ACCOUNTABILITY : POLICIES AND PROCEDURES | 
 | Element 2 | MANAGEMENT OF PERSONNEL | 
 |  | MANAGEMENT OF CONTRACTORS | 
 | Element 3 | PORT AND HARBOUR OPERATIONS | 67
 | Element 4 | TERMINAL LAYOUT - GENERAL | 
 |  | TERMINAL LAYOUT – TRANSFER EQUIPMENT | 
 | Element 5 | SHIP/SHORE INTERFACE | 
 | Element 6 | TRANSFER OPERATIONS | 
 | Element 7 | MAINTENANCE MANAGEMENT | 
 | Element 8 | MANAGEMENT OF CHANGE | 
 | Element 9 | INCIDENT INVESTIGATION AND ANALYSIS | 
 | Element 10 | MANAGEMENT OF SAFETY AND OCCUPATIONAL HEALTH | 
 |  | SECURITY MANAGEMENT INCLUDING VISITOR CONTROLS | 
 | Element 11 | ENVIRONMENTAL PROTECTION | 
 | Element 12 | EMERGENCY PREPAREDNESS | 
 | Element 13 | MANAGEMENT SYSTEM REVIEW | 
Optional | Element 14 | OPERATIONS AT BUOY MOORINGS | + 10
 | Element 15 | TERMINALS IMPACTED BY ICE OR SEVERE SUB-ZERO AIR TEMPERATURES | + 14
MTMSA