## Slide 1: HSE Requirements for Lifting Operations
Company Rule CR-GR-HSE-420
Notes: Afin de respecter la dénomination de la Marque, merci de veiller à la bonne orthographe de TotalEnergies.
TotalEnergies s’écrit en un seul mot, sans espace, avec un « s » à la fin, avec le T et le E en majuscules, les autres lettres en minuscules, et pas d’accent sur le E majuscule.
Elle s’écrit bien TotalEnergies et non :
Total Energies (avec un espace)
totalenergies
total energies
Totalenergies
Total energies
totalEnergies
total Energies
TOTALENERGIES
TOTAL ENERGIES

## Slide 2: CR-GR-HSE-420
Purpose:
This rule defines the minimum HSE requirements for the control of risks related to the preparation and execution of crane, rigging, and mechanical handling operations, on sites operated by entities of the Company.
It defines the technical aspects which must be taken into account for the performance of any craneage, rigging and mechanical handling operation at sea, on land, in coastal areas and underwater in terms of:
  Organisation, preparation and execution of lifting, slinging and handling operations;
  Training and competence of the persons involved in lifting, slinging and handling operations;
  Management of the lifting equipment used.
This rule has been approved by the HSE Committee on September 2022

## Slide 3: CR-GR-HSE-420
Because we realised that :
small lifting operations were not, in general, carried out with sufficient rigour;
the levels of preparation and planning (studies, procedures, risk analyses, etc.) very often left something to be desired;
The equipment used (appliances and accessories) was not always appropriate for the work to be carried out;
the supervision of operations was not, in some cases, adequate.
Our fundamental objective is twofold:
The first is to have more rigour and methodology in the preparation and control of any lifting operation;
The second is to improve the safety of operations.
If every step of the management process we want to put in place is followed, every lift should be done safely because :
it is part of an appropriate safety management system;
it is well planned;
the risks are known and properly assessed;
it is properly supervised; and
it is carried out by competent personnel using certified, maintained and appropriate equipment.
Why a Company Rule with the title “HSE Requirements for Lifting Operations”?

## Slide 4: Structure of the rule:
2
3
4
5
1
Management of lifting operations
Organisation
Management of lifting equipment
Planning and preparation of the lifting operations
Performing the lifting operations
5 themes
20 requirements
1 – Lifting Operations Management Procedure 2 – Categorisation and Management of Lifting Operations
3 – Competent Person for Lifting Operations 4 – Competencies and Training
5 – Certification of Lifting Equipment 6 – Lifting Equipment Register 7 – Maintenance Programme for Lifting Devices 8 – Periodic General Verification Report 9 – Visual Inspection before Use 10 – Logbook of Lifting Devices 11 – Lifting of Personnel
12 – Risk Analysis 13 – Lift Plan 14 – Review and Technical Validation of the Lift Plan 15 – Authorisation of Category 3 Lifting Operations over Live Installations or near Power Lines
16 – Monitoring of Lifting Operations 17 – Final Check before starting any Lifting Operation of a Suspended Load – Safe to Lift 18 – Restricting Access 19 – Control of the Movements of the Load 20 – Debriefing after the Lifting Operation

## Slide 5: Structure: 5 themes, 20 requirements

## Slide 6: Structure: 5 themes, 20 requirements
Effective Date: ▪ 12 months from the date of publication.
Scope of work:
This rule applies to all crane, rigging, and mechanical handling operations carried out using motorised or non-motorised lifting devices, owned by Company and/or run by external companies on installations operated by the Company's entities.
It applies to any operation where a load has to be lifted, lowered, turned or suspended. The lifting equipment concerned may be mobile cranes (self-propelled carrier cranes, self-propelled rough-terrain cranes, crawler cranes, auxiliary loading cranes, etc.), mobile and pedestal tower cranes, gantry cranes, pedestal cranes, offshore cranes, derricks, electric overhead cranes, gantry cranes, monorails, jib cranes, hoists, jacks, forklift trucks, excavators and mechanical shovers, etc.
It also applies to lifting accessories, including slings, chains, wire ropes, hooks, shackles, containers, baskets, skids and pallets.

## Slide 7: Why are there one CR and one GS with the same title?
Clarification of the requirements of CR-GR-HSE-420:
The requirements stated in CR-GR-HSE-420 are general, basic and are the minimum requirements for planning, preparing and performing a safe lifting operation.
Insofar as the Company is not the company in charge of carrying out the lifting operations, the lift plan, preparation, studies, control of equipment, manpower and supervision are the responsibility of the company in charge of the work and the persons competent to carry out these functions are its responsibility.
Why a Company Rule and a General Specification with the same title?
Because the Company Rule is for internal use and because it cannot be passed on to external companies.
As 80% of the requirements of the CR apply to external companies working on our entities, we have written a General Specification containing the requirements applicable only to the latter.
This general specification is transmitted to external companies and the entities and subsidiaries ensure that they comply with it.

## Slide 8: Presentation of the requirements
{Requirement 3.1.1: Lifting Operations Management Procedure
A procedure for the management of lifting operations based on the requirements of this rule is established and implemented by each entity or affiliate.
(Expectation 04.01)
Requirement 3.1.2: Categorisation and Management of Lifting Operations
Any lifting operations are categorised according to their level of criticality using the criteria defined in Appendix 3 and managed (organisation, documentation, monitoring) in compliance with the requirements of this rule and according to a management method described in Appendix 4: Category 1: simple lifting operation. Category 2: standard lifting operation. Category 3: critical lifting operation.
(Expectations 03.01, 03.04, 03.05, 04.10)

## Slide 9: Presentation of the requirements
Requirement 3.2.1: Competent Person for Lifting Operations
One or more persons competent to plan lifting operations, to validate lift plans and to monitor lifting operations are designated by the entity or affiliate. Their role and responsibilities according to their level of competence are defined in Appendix 2.
(Expectations 01.04)
Requirement 3.2.2: Competencies and Training
Any person involved (planner/preparer, lifting device operator, slinger, rigger, banksman, person in charge / lifting superintendent, etc.) in the preparation and execution of a lifting operation: is trained in accordance with his or her roles and responsibilities (see Appendix 2), holds the required authorisations.
(Expectations 06.01, 06.02) )

## Slide 10: Presentation of the requirements
{Requirement 3.3.1: Certification of Lifting Equipment
Any use of lifting equipment assumes that it has been designed, manufactured, certified, in accordance with international or local standards validated by the Technical Support of the Company, and has undergone a Periodic General Verification by a recognised inspection body in the country where the entity or affiliate operates, and approved by it. The certificate of conformity and/or the certificate of the initial overload test (if performed) of the lifting equipment is available on request at the place where the lifting operation is performed.
(Expectations 04.03, 05.08)
{Requirement 3.3.2: Lifting Equipment Register
Each entity or affiliate shall establish and maintain a register of lifting equipment owned or leased (long term hire) by it. At least, the following are recorded: Name of the manufacturer, description, type, and model. Serial number or unique identification number. Date of manufacture and date of first use. Dates of each load test and proof load test. Dates of periodic general inspections and detailed examinations (with the name of the inspector or examiner).
(Expectations 04.03, 05.08)

## Slide 11: Presentation of the requirements
Requirement 3.3.3: Maintenance Programme for Lifting Devices
A preventive, corrective, and conditional maintenance programme for the lifting devices belonging to the entity or affiliate is implemented. It considers the manufacturers’ recommendations and is adapted to the conditions of use (frequency and types of lifting, etc.) and to the age of the devices. The details and history of the maintenance interventions are recorded in an inspection and maintenance logbook established and maintained by each entity or affiliate. This logbook is available for consultation on request.
(Expectations 04.03, 05.08)
Requirement 3.3.4: Periodic General Verification Report
A valid periodic general verification report is available at the place where the lifting operation is performed, for any lifting equipment used, whether or not owned by the entity or affiliate.
(Expectations 04.03, 05.08)
Requirement 3.3.5: Visual Inspection Before Use
All lifting equipment is visually inspected by the operator of the lifting device or by the user of the lifting accessories before each use.
(Expectations 04.03, 05.08)

## Slide 12: Presentation of the requirements
{Requirement 3.3.6: Logbook of Lifting Devices
All non-portable lifting devices owned or leased by the entity or affiliate has a logbook in which all information relating to inspections, load tests, maintenance and repairs of the device is recorded in chronological order. The activities of offshore cranes, owned by the entity or affiliate, are recorded in this logbook in a specific section mentioning at least the: Date. Number of lifts carried out. Mass and range.
(Expectations 04.03, 05.08)
Requirement 3.3.7: Lifting of Personnel
The lifting of personnel is carried out exclusively with equipment specifically designed and certified for this purpose (Mobile Elevating Work Platforms [MEWPs], site lifts, suspended cradles, etc.).
(Expectation 03.04)

## Slide 13: Presentation of the requirements
Requirement 3.4.1: Risk Analysis
A risk analysis is carried out before any lifting operation. The level of detail of the risk analysis depends on the category (1, 2 and 3) of the lifting operation.
(Expectations 03.01, 03.04)
Requirement 3.4.2: Lift Plan
A lift plan is prepared for any lifting operation of a suspended load regardless of its category.
(Expectation 04.01)
Requirement 3.4.3: Review and Technical Validation of the Lift Plan
For any lifting operation, whatever its category, the lift plan is validated by the person in charge. For any category 3 operation, the lift plan is, in addition, technically validated by a competent person employed by the Company or contracted for this purpose.
(Expectations 04.01, 04.10)

## Slide 14: Presentation of the requirements
Requirement 3.4.4: Authorisation of Category 3 Lifting Operations Over Active Installations or near power lines
Category 3 lifting operations above active installations or in the vicinity of power lines, accompanied by the risk analysis and the lift plan, are subject to formal authorisation by the operations manager of the site.
(Expectations 04.01, 04.10)
Requirement 3.5.1: Monitoring of Lifting Operations
Category 3 lifting operations must be monitored by a competent person for this purpose, outside the lifting team, at the place of execution.
(Expectation 03.04)
Requirement 3.5.2: Final Check Before Starting any Lifting Operation of a suspended load - Safe To Lift
A checklist of operational controls is filled in before any lifting operation with a crane, or other lifting device begins.
(Expectation 03.04)

## Slide 15: Presentation of the requirements
Requirement 3.5.3: Restricting Access
Access to the lifting zone and to the lifting device is restricted and appropriately controlled and/or marked.
(Expectation 03.04)
Requirement 3. 5.4: Control of the Movements of the Load
The movements of the lifted load are controlled throughout the lifting operation. The control of the movements of the lifted load and its guidance (during take-off and set down) are not carried out by hand. Specific devices (retaining cables, guide ropes, pike poles, etc.) are used for this purpose. Their use must be subject to a prior risk assessment.
(Expectation 03.04)
Requirement 3.5.5: Debriefing After the Lifting Operation
As part of the continuous improvement of lifting operations, and to make them safer, a debriefing is carried out with all those involved at the end of any category 2 and 3 lifting operations.
(Expectation 08.04)